## Slide 1: AD9213 PCB layout with GSGSG RF Probe Pads GSGSG = Ground, Signal, Ground, Signal Ground)
ADC Package Outline (Dark Red Outline)
RF Probe Pad (5 Gold Rectangles)
RF Probe Pad is 42mil from package
edge and 71.5 mil from Solder Balls
Transmission Line Parameters
Total length of each transmission line, from solder balls to probe pad, is 76.6 mil
Zo = 50Ω Differential
Transmission line width is variable
24 mil from solder balls to separation point.
26 mil from separation point to probe pad.
The effects from the short traces on the board are not de-embedded from the measured parameters.
Additional details about the transmission lines can be defined by analyzing the Gerber layout files and PCB stackup provided below.