Hybrid DC to DC Power Converter Issues Overview:  Needs Vs. Supply Chain

# Authors:  Philip B. Gagne  - T3 Aerospace

## L. G. Zambotti  - T3 Aerospace

John W. Parker  - SAIC

Ken Jacobs - SAIC

## R. J. Reaney  - T3 Aerospace

John E. Pandolf  - NASA

# James F. Bockman - NASA

# Editor:  Jeannette Plante – Dynamic Range Corporation

#### Prepared for the NASA EEE Parts Assurance Group

May 20, 2005

Executive Summary

Our survey of Direct Current to Direct Current (DC to DC) hybrid power converter availability for NASA systems uncovered a staggering small quantity that are fully qualified for space use in a relatively healthy overall market.  The lack of reuse of electrical designs further frustrates our ability to find qualified product to satisfy all of the Agency’s converter needs.  Technology advances and new discoveries about semiconductor failure modes in the ionizing radiation environment of space continue to impede qualification of new part numbers.  Some new technology strategies such as the move toward more modular systems is expect to improve part reuse and reduce the need for new qualified parts.  Other technology advances such as low voltage, high speed chips will have the opposite effect.

Introduction

DC to DC Converters are used in civil and military aerospace equipment to provide regulated voltage and current sources to subsystems which are clients of the main system’s power bus.  In a typical satellite system, the solar arrays are designed to provide a 28V main bus voltage.  The subsystems need that voltage converted to levels that are applicable to their functionality: 5.0V, 3.3V and 2.5V for digital subsystems and ±12V and ±15V for analog subsystems.  Examples of typical satellite subsystem loads are a computer, a motor, a transmitter and a laser firing control system.  Other NASA spacecraft such as the Orbiter and the Space Station, have different bus voltages however their subsystems need the same 5.0V, 3.3V, ±12V and ±15V source voltages.  Power and regulation requirements vary widely across the various subsystem and spacecraft applications.  DC to DC converters are primary building blocks of the power system and critical nodes throughout the avionics of a spacecraft (Figure 1.).

In all spacecraft designs, mass and volume are rationed among the subsystems making miniaturization highly valued.  This has lead to a heightened demand for miniaturized DC to DC converters and many are offered on the market by many vendors.  Rather than building up a converter using discrete parts on a traditional printed circuit card, the converter, sometimes with electromagnetic interference (EMI) filter circuits included, is built up in a relatively small metal package using hybrid microcircuit electronic packaging technology.  These are referred to as hybrid DC to DC converters.   Hybrid DC to DC converters are sold in a variety of styles which vary foremost by input voltage, output voltage (single, dual and triple output voltages are offered), power efficiency and maximum output power.  The styles offered continually change to keep pace with the ever changing needs of the design community which includes space hardware designers.

The total space market for DC to DC Converters is small in comparison to the industrial, military and commercial markets yet the variety of product types required is high.  The result is that the vendors pick what they consider to be broadly applicable designs defined by what are considered in the commercial industry to be key discriminating characteristics:  power, physical size, number and types of outputs, and efficiency.  This concept that a few part types can be applied in a wide range of designs and that selection can be based on just a few characteristics keeps the “solution set” small and has actually led to power system functionality problems.   These problems arise from a common misconception in the industry that a “high” power converter can be used for all power needs from 0 to Pmax.  These converters are designed with an operational “sweet spot” based on load level and type, input impedance and other circuit/system conditions.  Use of the parts outside of this sweet spot has been found in several cases to lead to device instability and failure.  The trend toward increased power management directly at the consuming device rather than at the bus level may exacerbate application problems if it does not drive the qualification of new, special-purpose part types.

Space Market Analysis

The size of the current space electronics market can be estimated several ways, most common are the top down method, based upon total planned spacecraft, and the bottom-up approach that looks at the current sales of worldwide semiconductor electronics.

From a top down perspective the Aerospace Industries Association projected the aerospace market for 2002 at approximately $153 billion.  DoD accounted for $57 billion, NASA approximately $13 billion, $42 billion for civilian aircraft, and upgrades and maintenance accounted for the remaining sales.  NASA’s budget for aerospace in 2003 was $13.4 billion and projected to be $13.6 billion in 2004.  Estimating the size of the space hybrid DC to DC power converter market from this data requires determination of two factors.  First is the percentage of the aerospace market that is related to onboard power converters and the second the percentage of the aerospace market that is space related.  The first was estimated at 0.5% the latter at 32%.  Applying the first factor to the $153 billion total market provides an estimate of the entire aerospace hybrid DC to DC power converters including those for space.  The space related portion of the $765 million market is obtained by applying the second factor.  The top-down approach estimated that portion of the market at $245 million.

From a bottom-up perspective the 2003 total worldwide semiconductor market was projected at $166 billion.  These estimates are from multiple sources.  According to Semico Research Corporation the military portion of the market is 1.1% or $2.3 billion.  NASA and civilian space is estimated at an additional $630 million for a total military and space electronic market of $2.94 billion.  However, from this point the analysis is much more difficult.  The percentage of the military market that is space related is extremely difficult to determine.  Also the numbers only reflect the cost of semiconductor electronics and not the cost of assembly, non-semiconductor parts, testing, qualification, configuration management, and related space programmatics.  It is not unusual for space-based assemblies costing $100,000 to only have a semiconductor BOM (bill of material) valued at less than $25,000.  Our rough estimates using a bottom-up approach places the market for space hybrid DC to DC power converters between $250 million and $300 million.

Therefore, based upon the two approaches we estimate the hybrid DC to DC power converter market in the range of $200 million to $300 million.

Availability of Space Grade Product Through the Mil-Spec System

In the absence of a NASA specification and qualification system for electronic parts, the Agency leverages heavily off of the military specification (mil-spec) system and measures availability of products for space systems with respect to that system.  The Defense Supply Center Columbus (DSCC) is the logistics management organization for military specifications for electronic parts including hybrid microcircuits, of which DC/DC converters are one type.  There are thirty-nine manufacturers listed by DSCC in their QML-38534 Hybrid Microcircuit Program Status as of August 2004.  Table 1 shows the manufacturers DSCC has certified as of the 3rd quarter of 2004 as having a production line process that meets the requirements of MIL-PRF-38534, Hybrid Microcircuits, General Specification for.  This list applies for all types of hybrid microcircuits in the mil-spec system, not just DC to DC converters.  There are six DSCC-certified lines that are active in the power/DC to DC converter area:  Aeroflex, Crane Interpoint, International Rectifier, M.S.Kennedy, Natel Engineering and VPT/Delta.

MIL-PRF-38534E defines requirements based on two levels of intended application:  one for high reliability ground and aeronautics applications (standard military level or Class H) and one for high reliability space (Class K) (see paragraph 1.3 Classification of the specification).  DSCC has clarified the standard military level as “designed to be used only in non-space applications”.  The assumption that Class H devices can be replaced when they fail in service is a factored into the way they are specified and built, therefore, MIL-PRF-38534 Class K devices are considered preferred for space use on the basis of risk of failure.

Class K devices, though preferred for space use, may not be guaranteed for a Total Ionizing Dose (TID) radiation tolerance level above 50 kRads(Si) or any level of protection in an energetic particle (Single Event Effect, SEE) environment.  Further, though these devices have long been tested and approved for use in space, recent discoveries have found that these devices may not be as radiation hard as prior high dose rate testing has indicated due to the low dose rate or ELDRS (Extremely Low Dose Rate Sensitivity) effect.  This has created a renewed concern over the type of testing that needs to be applied to assure that the linear devices inside of DC to DC converters are sufficiently radiation hard whether they are of mil-spec pedigree or not.

In order to be able to sell a Class K DC to DC converter, the vendor must first have their production line “certified” by DSCC to produce MIL-PRF-38534 product.  Then, they must have a part specification (Standard Military Drawing, SMD) written for the specific part they will sell.  Successful testing to the electrical specifications of the SMD and the overall quality and reliability program defined in MIL-PRF-38534, to the Class K level, then allows them to mark and sell DC to DC converters with the SMD part number and the Class K “brand”.   Though a relatively large number of vendors are certified to make Class H and Class K MIL-PRF-38534 Hybrids, only one source (Crane Interpoint Corporation) has completed the entire program, through SMD and qualification, for Class K DC to DC Converters.  Appendix A contains every Class K, DC to DC power converter readily available for procurement.  Table 2 describes the available Class K DC to DC converters according to their input voltage and output power.  The relatively small number of products that have passed through the entire QML-K process often lead NASA projects to buying non-SMD part numbers to satisfy their needs.  The dual approach of using standard and non-standard parts in space systems, has at times reduced the use of the few Class-K part numbers that are available and directs NASA procurement dollars away from investment in qualifying new part numbers.

Table 1:  DSCC Certified Vendors for MIL-PRF-38534 Product

| Advanced Analog IR | Aeroflex Microelectronic Solutions |
| --- | --- |
| Agilent Technologies | Analog Devices Incorporated |
| Apex Microtechnology | Austin Semiconductor, Inc. |
| BAE Platform Solutions | BI Technologies Corporation |
| Boeing Defense and Space Group | C-MAC Microcircuits Limited |
| CMC Electronics Cincinnati | CMC Electronics Incorporated |
| Cougar Components | Crane Interpoint |
| DDC Ireland LTD. | Data Device Corporation |
| Datel Incorporated | EMS Technologies Incorporated |
| Hytek Microsystems Incorporated | International Rectifier Corporation |
| Interpoint Taiwan Corporation | Lockheed Martin Missiles and Fire Control |
| M.S. Kennedy Corporation | MPC Products Corporation |
| Micro Networks Company | Micro-Precision Technologies, Inc. |
| Micropac Industries, Incorporated | Natel Engineering Company, Inc. |
| National Hybrid, Incorporated | REMEC Components – Palm Bay |
| REMEC Incorporated | Raytheon Systems Limited |
| Satcon Electronics | Sensitron Semiconductor |
| Solitron Devices, Incorporated | Teledyne Electronic Technologies |
| VPT/Delta | Warner Robins ALC/LYP |
| White Electronic Designs Corporation |  |

The “off-the-shelf” certification, radiation data and electrical characterization that comes with MIL-PRF-38534, Class K devices dramatically shortens procurement lead time and lowers cost as compared to lead time and cost for comparable devices that are not sold within the mil-spec system.  To buy a comparable part outside of the mil-spec system using a Source Control Drawing (SCD) or to buy a new design within the mil-spec system by creating a new SMD requires a nominal 26 weeks for creating and coordinating the drawing and finalizing the design parameters and another 60 weeks for manufacturing.  An 18 to 24 month lead time for a DC to DC converter is usually considered problematic in the context of a flight mission schedule.  Many space programs don’t have the luxury to incur a long-lead procurement for such a critical part.  Projects that can take advantage of off-the-shelf, Class K part numbers can realize a great schedule advantage over those who decide to, or must, create an SCD or SMD for their purchase.

Table 2: Interpoint Class K DC to DC Converter Types

| Family Name | Vin (VDC) | Vout (VDC) | Power |
| --- | --- | --- | --- |
| SLH | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 1.5 Watts |
| SMFL | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 65 Watts |
| SMFLHP | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 100 Watts |
| SMHF | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 15 Watts |
| SMSA | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 5 Watts |
| SMTR | 28 | Single: 3.3, 5, 12, 15 Dual: ±5, ±12, ±15 | 30 Watts |

Cost and performance are also big drivers when embarking on a new SCD/SMD-based procurement.  Past experience shows costs to run from $200K to $500K for this type of effort depending on the hybrid complexity and technical support required during design and qualification testing; the cost and lead-time for a printed circuit board (discrete) design and a custom hybrid power converter build can be about the same.  It is quite common that existing designs are modified or “tweaked” to meet the electrical performance specifications in the new SCD.  The impact of the modification on electrical performance over a wide range of operating conditions may be logistically difficult to determine and again, cost prohibitive.  The impact the change will have on the long term reliability of the overall part and primary failure modes may be practically impossible to understand within the timeframe of the project.

Future Needs

The market for commercial, portable electronics produces a high demand for low voltage and low power microcircuits.  Reduced transistor feature size is a key enabler allowing both existing circuits to occupy a smaller physical space on the chip and the addition of new features with no increase in footprint.  Lower voltage thresholds enable higher switching frequencies which extends the capability of data and signal processors.  The space industry benefits from this technological trend by being able to pack increased functionality and complexity into limited mass and volume allocations.  An example of this concept is shown in Figure 2.  Another example is the trend toward more data processing functionality in flight instruments rather than accomplishing data processing primarily on the ground.  With this increased complexity and operating frequency comes an increase in the circuit power dissipation.

Figure 2: Following the trend in semiconductor density, it is feasible to reduce spacecraft C&DH electronics significantly, eventually achieving a “spacecraft on a chip” implementation.

As described above, semiconductor technology and system engineering trends are expected to continue to change critical operational requirements for DC to DC converters for future spaceflight hardware.  Newly discovered failure mechanisms such as those associated with ELDRS or trapped charges attendant to nuclear events that constitute “Van Allen belt-like” conditions, are also driving new test and performance requirements.  Even though low voltage electronics would appear to reduce the payload’s heat, the very high switching speeds drive up overall power and thermal dissipation.  Very low noise becomes critical in low voltage circuits and will cause the need for closer examination of maximum ripple specifications (1% ripple of a 2V output is only 10 to 20 millivolts).

Modularity is increasingly being considered as a strategy to combat a lack of market share and the continual re-development of power supply components for a wide range of system topologies (Figure 3).  Versatile electrical and mechanical interfaces that integrate easily into higher-level assemblies enable design reuse.  The bus and payload power converter must be able to work in a complementary fashion to provide all the required voltage levels and regulation while maintaining stability and low system noise.  Technologies such as programmability, increased radiation tolerance (both total ionizing dose to a minimum level of 100 kRads(Si) and single event effects with a minimum upset resistance to particles of 37 MeV), modularity and increased volumetric efficiency (W/m3) have all been identified as key enabling features for future high performance, highly reusable systems.

Figure 3:  Family of power elements

Conclusions

This overview broadly discusses the needs driving the use of DC to DC converters in space systems, existing and preferred procurement strategies, and performance and assurance issues associated with DC to DC converter use.  It also touches on the size of the DC to DC converter component of the aerospace electronic parts industry and availability of space grade product.  This paper demonstrates the need for more manufacturers, as there is currently only one source for off-the-shelf, space-grade product (Crane Interpoint).  The demand for new, lower voltage levels while improving reliability and immunity to strenuous aerospace environments creates a high entrance barrier to new vendors and slows the increase in new space-grade part numbers from certified shops.  With the low number of available Class K qualified part numbers and MIL-PRF-38534-certified vendors, flight projects continue to face long lead times and higher costs in order to obtain flight-ready parts via SCD’s or new SMD’s.  Working with the qualified suppliers giving them the necessary requirement needs and information before project procurement cycles begin is the key to reducing this problem.

APPENDIX A

| K Level Certified/Qualified Microcircuit DC/DC Converters for Space Applications |
| --- |
| DSCC# | DATE | MANUFACTURER | PART # |
| 5962L0052601KXA | 12/16/02 | Interpoint | SLH2805S |
| 5962L0052601KXC | 12/16/02 | Interpoint | SLH2805S |
| 5962R0052601KXA | 12/16/02 | Interpoint | SLH2805S |
| 5962R0052601KXC | 12/16/02 | Interpoint | SLH2805S |
| 5962L0052701KXA | 2/7/01 | Interpoint | SLH2812S |
| 5962L0052701KXC | 2/7/01 | Interpoint | SLH2812S |
| 5962R0052701KXH | 2/7/01 | Interpoint | SLH2812S |
| 5962R0052701KXC | 2/7/01 | Interpoint | SLH2812S |
| 5962L0052801KXA | 12/16/02 | Interpoint | SLH2815S |
| 5962L0052801KXC | 12/16/02 | Interpoint | SLH2815S |
| 5962R0052801KXA | 12/16/02 | Interpoint | SLH2815S |
| 5962R0052801KXC | 12/16/02 | Interpoint | SLH2815S |
| 5962R0150102KXA | 10/26/01 | Interpoint | SMTR283R35 |
| 5962R0150102KXC | 10/26/01 | Interpoint | SMTR283R35 |
| 5962R0150102KZA | 10/26/01 | Interpoint | SMTR283R3SF |
| 5962R0150102KZC | 10/26/01 | Interpoint | SMTR283R3SF |
| 5962R0250401KXA | 12/11/01 | Interpoint | SLH2805D |
| 5962R0250401KXC | 12/11/01 | Interpoint | SLH2805D |
| 5962L0251002KXA | 1/15/03 | Interpoint | SMHF283R3S |
| 5962L0251002KXC | 1/15/03 | Interpoint | SMHF283R3S |
| 5962R0251002KXA | 1/15/03 | Interpoint | SMHF283R3S |
| 5962R0251002KXC | 1/15/03 | Interpoint | SMHF283R3S |
| 5962L0251002KZA | 1/15/03 | Interpoint | SMHF283R3SF |
| 5962L0251002KZC | 1/15/03 | Interpoint | SMHF283R3SF |
| 5962R0251002KZA | 1/15/03 | Interpoint | SMHF283R3SF |
| 5962R0251002KZC | 1/15/03 | Interpoint | SMHF283R3SF |
| 5962L9160102KXA | 10/2/03 | Interpoint | SMHF2815S |
| 5962L9160102KXC | 10/2/03 | Interpoint | SMHF2815S |
| 5962R9160102KXA | 10/2/03 | Interpoint | SMHF2815S |
| 5962R9160102KXC | 10/2/03 | Interpoint | SMHF2815S |
| 5962L9160102KZA | 10/2/03 | Interpoint | SMHF2815SF |
| 5962L9160102KZC | 10/2/03 | Interpoint | SMHF2815SF |
| 5962R9160102KZA | 10/2/03 | Interpoint | SMHF2815SF |
| 5962R9160102KZC | 10/2/03 | Interpoint | SMHF2815SF |
| 5962L9161402KXA | 10/14/03 | Interpoint | SMHF2815D |
| 5962L9161402KXC | 10/14/03 | Interpoint | SMHF2815D |
| 5962R9161402KXA | 10/14/03 | Interpoint | SMHF2815D |
| 5962R9161402KXC | 10/14/03 | Interpoint | SMHF2815D |
| 5962L9161402KZA | 10/14/03 | Interpoint | SMHF2815DF |
| 5962L9161402KZC | 10/14/03 | Interpoint | SMHF2815DF |
| 5962R9161402KZA | 10/14/03 | Interpoint | SMHF2815DF |
| 5962R9161402KZC | 10/14/03 | Interpoint | SMHF2815DF |
| 5962L9213902KXA | 6/26/00 | Interpoint | SMHF2805S |
| 5962L9213902KXC | 6/26/00 | Interpoint | SMHF2805S |
| 5962R9213902KXA | 6/26/00 | Interpoint | SMHF2805S |
| 5962R9213902KXC | 6/26/00 | Interpoint | SMHF2805S |
| 5962L92130902KZA | 6/26/00 | Interpoint | SMHF2805SF |
| 5962L92130902KZC | 6/26/00 | Interpoint | SMHF2805SF |
| 5962R92130902KZA | 6/26/00 | Interpoint | SMHF2805SF |
| 5962R92130902KZC | 6/26/00 | Interpoint | SMHF2805SF |
| 5962L9214402KXA | 11/6/03 | Interpoint | SMHF2812D |
| 5962L9214402KXC | 11/6/03 | Interpoint | SMHF2812D |
| 5962R9214402KXA | 11/6/03 | Interpoint | SMHF2812D |
| 5962R9214402KXC | 11/6/03 | Interpoint | SMHF2812D |
| 5962L9214402KZA | 11/6/03 | Interpoint | SMHF2812DF |
| 5962L9214402KZC | 11/6/03 | Interpoint | SMHF2812DF |
| 5962R9214402KZA | 11/6/03 | Interpoint | SMHF2812DF |
| 5962R9214402KZC | 11/6/03 | Interpoint | SMHF2812DF |
| 5962L9306802KXA | 4/26/00 | Interpoint | SMTR2805S |
| 5962L9306802KXC | 4/26/00 | Interpoint | SMTR2805S |
| 5962R9306802KXA | 4/26/00 | Interpoint | SMTR2805S |
| 5962R9306802KXC | 4/26/00 | Interpoint | SMTR2805S |
| 5962L9306802KZA | 4/26/00 | Interpoint | SMTR2805SF |
| 5962L9306802KZC | 4/26/00 | Interpoint | SMTR2805SF |
| 5962R9306802KZA | 4/26/00 | Interpoint | SMTR2805SF |
| 5962R9306802KZC | 4/26/00 | Interpoint | SMTR2805SF |
| 5962L9306902KXA | 6/21/00 | Interpoint | SMTR2812S |
| 5962L9306902KXC | 6/21/00 | Interpoint | SMTR2812S |
| 5962R9306902KXA | 6/21/00 | Interpoint | SMTR2812S |
| 5962R9306902KXC | 6/21/00 | Interpoint | SMTR2812S |
| 5962L9306902KZA | 6/21/00 | Interpoint | SMTR2812SF |
| 5962L9306902KZC | 6/21/00 | Interpoint | SMTR2812SF |
| 5962R9306902KZA | 6/21/00 | Interpoint | SMTR2812SF |
| 5962R9306902KZC | 6/21/00 | Interpoint | SMTR2812SF |
| 5962L9307002KXA | 6/22/00 | Interpoint | SMTR2815S |
| 5962L9307002KXC | 6/22/00 | Interpoint | SMTR2815S |
| 5962R9307002KXA | 6/22/00 | Interpoint | SMTR2815S |
| 5962R9307002KXC | 6/22/00 | Interpoint | SMTR2815S |
| 5962L9307002KZA | 6/22/00 | Interpoint | SMTR2815SF |
| 5962L9307002KZC | 6/22/00 | Interpoint | SMTR2815SF |
| 5962R9307002KZA | 6/22/00 | Interpoint | SMTR2815SF |
| 5962R9307002KZC | 6/22/00 | Interpoint | SMTR2815SF |
| 5962L9308902KXA | 5/21/01 | Interpoint | SMSA2812D |
| 5962L9308902KXC | 5/21/01 | Interpoint | SMSA2812D |
| 5962R9308902KXA | 5/21/01 | Interpoint | SMSA2812D |
| 5962R9308902KXC | 5/21/01 | Interpoint | SMSA2812D |
| 5962L9309002KXA | 7/10/01 | Interpoint | SMSA2815D |
| 5962L9309002KXC | 7/10/01 | Interpoint | SMSA2815D |
| 5962R9309002KXA | 7/10/01 | Interpoint | SMSA2815D |
| 5962R9309002KXC | 7/10/01 | Interpoint | SMSA2815D |
| 5962L9309202KXA | 2/6/01 | Interpoint | SMSA2805S |
| 5962L9309202KXC | 2/6/01 | Interpoint | SMSA2805S |
| 5962R9309202KXA | 2/6/01 | Interpoint | SMSA2805S |
| 5962R9309202KXC | 2/6/01 | Interpoint | SMSA2805S |
| 5962L9309302KXA | 10/23/00 | Interpoint | SMSA2812S |
| 5962L9309302KXC | 10/23/00 | Interpoint | SMSA2812S |
| 5962R9309302KXA | 10/23/00 | Interpoint | SMSA2812S |
| 5962R9309302KXC | 10/23/00 | Interpoint | SMSA2812S |
| 5962L9309402KXA | 2/6/01 | Interpoint | SMSA2815S |
| 5962L9309402KXC | 2/6/01 | Interpoint | SMSA2815S |
| 5962R9309402KXA | 2/6/01 | Interpoint | SMSA2815S |
| 5962R9309402KXC | 2/6/01 | Interpoint | SMSA2815S |
| 5962R9316302KTA | 6/21/02 | Interpoint | SMFL2805SW |
| 5962R9316302KTC | 6/21/02 | Interpoint | SMFL2805SW |
| 5962R9316302KUA | 6/21/02 | Interpoint | SMFL2805SV |
| 5962R9316302KUC | 6/21/02 | Interpoint | SMFL2805SV |
| 5962R9316302KXA | 6/21/02 | Interpoint | SMFL2805S |
| 5962R9316302KXC | 6/21/02 | Interpoint | SMFL2805S |
| 5962R9316302KYA | 6/21/02 | Interpoint | SMFL2805SY |
| 5962R9316302KYC | 6/21/02 | Interpoint | SMFL2805SY |
| 5962R9316302KZA | 6/21/02 | Interpoint | SMFL2805SZ |
| 5962R9316302KZC | 6/21/02 | Interpoint | SMFL2805SZ |
| 5962R9319302KTA | 6/21/02 | Interpoint | SMFL2815DW |
| 5962R9319302KTC | 6/21/02 | Interpoint | SMFL2815DW |
| 5962R9319302KUA | 6/21/02 | Interpoint | SMFL2815DW |
| 5962R9319302KUC | 6/21/02 | Interpoint | SMFL2815DW |
| 5962R9319302KXA | 6/21/02 | Interpoint | SMFL2815D |
| 5962R9319302KXC | 6/21/02 | Interpoint | SMFL2815D |
| 5962R9319302KYA | 6/21/02 | Interpoint | SMFL2815DY |
| 5962R9319302KYC | 6/21/02 | Interpoint | SMFL2815DY |
| 5962R9319302KZA | 6/21/02 | Interpoint | SMFL2815DZ |
| 5962R9319302KZC | 6/21/02 | Interpoint | SMFL2815DZ |
| 5962L9852901KXA | 2/7/01 | Interpoint | SLH2815D |
| 5962L9852901KXC | 2/7/01 | Interpoint | SLH2815D |
| 5962R9852901KXA | 2/7/01 | Interpoint | SLH2815D |
| 5962R9852901KXC | 2/7/01 | Interpoint | SLH2815D |
| 5962L9955601KXA | 8/4/00 | Interpoint | SLH2812D |
| 5962L9955601KXC | 8/4/00 | Interpoint | SLH2812D |
| 5962R9955601KXA | 8/4/00 | Interpoint | SLH2812D |
| 5962R9955601KXC | 8/4/00 | Interpoint | SLH2812D |

###### APPLICABLE DOCUMENT SOURCES

- “Capacitor Applications In Switching Power Supplies”, J. Maxwell, March 15, 1995, sponsored by IEEE.

- “Comparison of PWM Zero Voltage Switching DC-DC Converters with Output Isolation”, J. Qian, October 10, 1995, sponsored by IEEE.

- “Test and Evaluation of Load Converter Topologies Used in SSF Power Management and Distribution DC Test Bed”, R.C. Lebron, August 1991, sponsored by IECEC.

- “A New Three-Phase AC-DC Zero Voltage Switching Isolated Converter Operating In DCM”, Y.V. Panov, October 10, 1995; sponsored by IEEE.

- “DV/DT-Current Handling Capabilities of SMPS MLC Capacitors”, S.P Cygan, March 16, 1992, sponsored by IEEE.

- “Subsystem Integration For Efficient Power Flow in 21st Century Airlifters”, D.K. Lindner, September 1, 1999, sponsored by AFRL-SR-BL.

- “Understanding Reliability In Commercial Power Converters”, A. Simopoulos. March 1993, sponsored by Hearst Business Publications.

- “Multikilowatt Power Electronics Development For Spacecraft”, D.K. Decker, August 1991, sponsored by IECEC.

- “Multilevel Converters - A New Breed Of Power Converters”, J.S. Lai, October 10, 1995, sponsored By IEEE.

- “Improving The Frequency Response of Ceramic Dielectrics For High Power Applications In Power Electronic Converters”, C. Campbell, December 1996, sponsored by IEEE.

- “Radiation Effects on DC-DC Converters”, J.O. Attia, August 1, 1999, sponsored by Prairie View Agricultural and Mechanical College.

- “Application Of IIIV Power Devices For DC/DC Power Conversion”, S. Ajram, January 4, 1996, sponsored by Universite des Sciences et Technologies de Lille.

- “Frequency-Based Load Sharing In Current-Mode-Controlled Buck Converters”, J.E. Moore, March 1 1999, sponsored by the Naval Postgraduate School.

- “Enhancing Reliability Of Board Mounted Power Modules Through End-To-End Process Improvement”, R.J. Brandt, March 16, 1992, sponsored by IEEE.

- “Effect Results for Microelectronics”, Martha O’Brien & Christina Seidleck of Raytheon Sys. Lanham, MD, Kenneth Label, Donald Hawkins, Janet Barth, Robert Reed & Cheryl Marshall of NASA/GSFC, Greenbelt, MD, Jim Howard  & Hak Kim of J&T Seabrook, MD. 1999 NSREC Data Workshop.

- “Radiation Testing Results of COTS Based Space Microelectronics”, 1999 NSREC Data Workshop.

- “The Effects of Space Radiation and Burn-In on Plastic Encapsulated Semiconductors”, 1999 NSREC Data Workshop.

- “Radiation Evaluation of Plastic Encapsulated Transistors and Microcircuits for Use in Space Applications”, 1999 NSREC Data Workshop.

- “Device SEE Susceptibility Update”, 1996-1998, 1999 NSREC Data Workshop

- IEEE Nuclear Science, Dec 2000, Volume 47, Number 6, Part II of IV Parts, Page 2039 & 2045.

- IEEE Nuclear Science, Dec 2000, Volume 47, Number 6, Part I of IV Parts, Page 1872 & 1879.

- NSREC Data Workshop, 2000, Page 6, 32, 53, 100, 106 & 123.

- IEEE NSREC Short Course, 2000, Section IV.

- Proceedings European Space Components Conference ESCCON 2000:

  - “Very Fine Line Technology for MCM-C Manufacturing Evaluation and Industrialization”, O. Puig, CNES, France and D. Samson, Matra Marconi Space, France, P 39.

  - “Power Modules: A Novel Approach to Achieve Compact Solutions for Complex Power Conditioning Circuits”, M. Perusini, and G. Tommaso, Alenia Aerospazio S.p.A., Italy, P45.

  - “Theoretical and Empirical Verification of the Stress Distribution in Stacked Ceramic Capacitors for Space Applications”, T. Kraft, Th. Gaul, R, Loffler, and R, Theis, BoschTelecom GmbH, Germany, P71.

  - “Supercapacitors: Applications and Requirements”, H. Barde, MMS, France P 79

  - “A Structured Procedure For Assessing the Suitability of Commercial Components for Space Applications”, P109, 115, 121, 125, 131, 143, 151, 277.

  - “Temperature Uprating Study on Use of Commercial Components for Space Applications”, Ph. Lay, C. Aicardi, B. Pasquier, P. Prodhomme, P. Carton, and P. LeBlanc, P.Lab. Central des Industries Electriques, France; CNES, France; Thomson CSF-TTM, France, Matra Marconi Space, France, P115.

  - “Establishment of Derating  Rules and Worst Case Analysis Figures for EEE Components”, L. Cosqueric, P. LeBlanc, G. Salveterra, L. Toudret, Matra Marconi Space, France, P121.

  - “Procurement of Catalogue Hybrid DC/DC Converters for Various Space Projects”, T. Liebler, B. Stradler, Bosch Telecom GmbH, Germany, P131.

# Text boxes

Figure 1:  Typical NASA Space Instrument Power System

Inhibit Control or Sequencing

Inhibit Control or Sequencing

Inhibit Control or Sequencing

Spacecraft

Power Bus

Current Limiting

EMI Filter  (internal)

EMI Filter  (internal)

+/- 15 Volt Hybrid DC to DC Converter

+5 Volt Hybrid DC to DC Converter

+3.3 Volt Hybrid DC to DC Converter

EMI Filter (external)

EMI Filter  (internal)

Spacecraft Subsystem

Communications

Memory

Processor

Command & Data Handling

Sensors