|  |  |  | REVISIONS |  |  |
| --- | --- | --- | --- | --- | --- |
|  | Rev | ECN | Description | Date | Approved |
|  | 1 |  | Preliminary | 3-15-00 | F. Palla |
|  | A | C01289 | Release to production | 4-24-01 | A. Perez |
|  |  | T |  |  |  |
| Approvals | Date | (BULLET 3 “F” CON.) Trimble specifications |  |  |  |
| DRAWN |  |  |  |  |  |
| CHECKED |  | Sheet | Size | Drawing Number | Revision |
| ISSUED |  | 1 of 6 | A | 41556-00-SP | A |

TRIMBLE NAVIGATION

BULLET ANTENNA

GPS ANTENNA WITH LOW NOISE AMPLIFIER

Part Number 41556-00

Part Number 41556-00-SP

Copyright ( 1995

Trimble Navigation Limited

645 North Mary Avenue

Sunnyvale, CA  94088

All rights reserved

| SPECIFICATION FOR GPS ANTENNA WITH LOW NOISE AMPLIFIER |  |
| --- | --- |
| 1.0 | APPLICATION |
|  |  | THIS SPECIFICATION DESCRIBES THE ELECTRICAL AND MECHANICAL CONDITIONS OF THE TRIMBLE MINIATURE ANTENNA, P/N 41556-00 |
| 2.0 | SYSTEM |
|  | THIS ANTENNA SYSTEM CONSISTS OF TWO FUNCTIONAL BLOCKS LISTED BELOW. |
|  | 2.1 | ANTENNA ELEMENT |
|  | 2.2 | LNA |
| 3.0 | GENERAL |
|  | 3.1 | ENVIRONMENTAL CONDITIONS |
|  |  | 3.1.1 | OPERATING TEMPERATURE | -40(C TO +85(C |
|  |  | 3.1.2 | STORAGE TEMPERATURE | -40(C TO +100(C |
|  |  | 3.1.3 | RELATIVE HUMIDITY | 20% TO 95% |
|  | 3.2 | ELECTRICAL SPECIFICATIONS |
|  |  | 3.2.1 | INPUT VOLTAGE | 5.0VV |
|  |  | 3.2.2 | POWER CONSUMPTION | 30mA MAX. |
|  |  | 3.2.3 | OUTPUT CONNECTOR | “F” CONNECTOR |
|  | 3.3 | MECHANICAL SPECIFICATIONS |
|  |  | 3.3.1 | MOUNTING | NUT MOUNT |
|  |  | 3.3.2 | WATER PROOF | WATER PROOF (JISD0203 S2) |
|  |  | 3.3.3 | SHOCK | 50G : VERTICAL AXIS 30G : ALL AXIS |
|  |  | 3.3.4 | VIBRATION | 10 ~ 200Hz. LOG SWEEP 3.0G (SWEEP TIME : 15 MIN.) 3 AXIS |
|  |  | 3.3.5 | ANTI-COROSION | BASED ON JIS Z 2371, SPRAY 5% SALT WATER 35(C SHOULD NOT RUST AFTER 96Hrs, |
|  |  | 3.3.6 | CONFIGURATION AND DIMENSION | SEE MECHANICAL DRAWING |
|  |  | 3.3.7 | WEIGHT | 170g |

| SPECIFICATION FOR GPS ANTENNA WITH LOW NOISE AMPLIFIER |
| --- |
| 4.0 | ANTENNA |
|  | 4.1 | FREQUENCY RANGE | 1,575,42+/-1.023MHz |
|  | 4.2 | GAIN | 90( : 3.0dBi MIN. 20( : -5.0dBi MIN. |
|  | 4.3 | POLARIZATION | RHCP |
|  | 4.4 | AXIAL RATIO | 90( : 4.0dB MAX. 10( : 6.0dB MAX. |
| 5.0 | LNA |
|  | 5.1 | FREQUENCY RANGE | 1,575,42+/-1.023MHz |
|  | 5.2 | GAIN | 313dB MAX. (+25(C(C) |
|  | 5.3 | NOISE FIGURE | 3.3dB MAX. (+25(C5(C) 3.8dB MAX. (+85(C) |
|  | 5.4 | OUT OF BAND REJECTION | ((=1,575.42MHz |
|  |  |  |  | ((+/-20MHz | 7dB MIN. |
|  |  |  |  | ((+/-30MHz | 12dB MIN. |
|  |  |  |  | ((+/-50MHz | 20dB MIN. |
|  |  |  |  | ((+/-100MHz | 30dB MIN. |
|  | 5.5 | OUTPUT IMPEDANCE | 50( |
|  | 5.6 | OUTPUT VSWR | 2.0MAX. |
| 6.0 | OVERALL SPECIFICATIONS (THROUGH ANTENNA, LNA, CABLE AND CONNECTOR) |
|  | 6.1 | FREQUENCY RANGE | 1,575,42+/-1.023MHz |
|  | 6.2 | GAIN | 35 3dBi (+25(C5(C) TEMP. DRIFT 1.5dBi |
|  | 6.3 | OUTPUT IMPEDANCE | 50( |
|  | 6.4 | VSWR | 2.0MAX. |
|  | 6.5 | OSCILLATION | NO OSCILLATION MUST BE FOUND IN BAND AND OUTBAND. |
| 7.0 | MTBF | TBD |
| 8.0 | RECOMMENDED STORAGE CONDITION AND STORAGE TERM | STORE IN ROOM CONDITION AS LISTED BELOW: TEMPERATURE -20(C(+45(C, HUMIDITY 80% MAX. |
| 9.0 | RELIABILITY TEST | TBD |
| 10.0 | EXTERNAL APPEAR ANCE | NO STAIN OR FLAW MUST BE FOUND. |
| 11.0 | CNNECTOR SPEC IMPEDANCE FREQUENCY RANGE WORKING VOLTAGE DIELECTRIC WITHSTANDING VOLTAGE VSWR CONTACT RESISTANCE 11.7 INSULATION RESISTANCE | 50 ohm 0-2 GHz 500Volt rms 1500Volts rms 1.3MAX 0-2GHz CENTER CONTACT 1.5 milliohms OUTER CONTACT 0.2milliohms 5000 megohms (min) |

12.0	DATA							GAIN (AT 5.0V0.2V f=1575MHz) AND

# POWER CONSUMPTION AT ROOM

TEMPERATURE.