Key Features

and Benefits

• Ovenized quartz

oscillator provides

clean 10 MHz (1 PPS)

signal that maximizes

bandwidth

• Combined GPS receiver

and ovenized oscillator

minimizes size and cost

• High volume manufac-

turing provides reliable

low-cost products

Thunderbolt GPS Disciplined Clock

Precise GPS Clock for Wireless Infrastructure

The Thunderbolt™GPS

Disciplined Clock is Trimble’s

latest offering for GPS synchro-

nization devices targeting the

wireless infrastructure. This

fourth-generation GPS clock

combines an 8-channel GPS

receiver, control circuitry and a

high-quality ovenized oscillator

on a single board, providing

increased integrity and reliability

at a lower size and cost.

The GPS clock’s level of

integration makes it a perfect

solution for precise timing appli-

cations in the wireless industry.

Among its uses are synchronizing

the E911 positioning infrastruc-

ture and maximizing bandwidth	Trimble’s Thunderbolt GPS Disciplined Clock in enclosure, and board form.

for wireless local loop.

The architecture is compara-

ble to systems currently used to

maintain the tough CDMA

holdover speciﬁcation. This

makes the Thunderbolt GPS

clock a natural for a CDMA

clock, the digital standard for

cellular phones.

Trimble’s approach is

unique. The Thunderbolt GPS

Clock outputs a 10 MHz refer-

ence signal and a 1 PPS signal

with an over-determined solution

synchronized to GPS or UTC

time. The 10 MHz reference

accommodates applications

requiring sub-microsecond tim-

ing. A single microprocessor per-

forms both the GPS navigation

and oscillator disciplining func-

tions. The GPS receiver is driven

directly by the 10 MHz output

signal of the oscillator. This is

calibrated against the incoming

GPS signal, with the resulting

clock and frequency measure-

ments fed into the oscillator

frequency control algorithm.

The T-RAIM (Time-

Receiver Autonomous Integrity

Monitor) algorithm is used to

monitor satellites to ensure signal

integrity.

Matching the Thunderbolt GPS

Clock with Trimble’s Bullet™

antenna creates a system that

provides reliable performance in

hostile environments. The system

can be easily calibrated for different

cable lengths.

The high level of integration

and volume production tech-

niques make the Thunderbolt

GPS Disciplined Clock an

extremely cost-competitive

timing solution for volume

synchronization applications.

Thank you for trying PDF-file.

Please note that PDF-file trial version converts only the first page of your document.

To convert your complete document, you need to purchase PDF-file.

To order, please visit: http://www.pdf-file.com/order_form.asp