TrimTrac Locator

Technical Manual

Including Enhanced Features and

Vehicle Adapter Module

(Applies to Firmware 1.08 and later)

Part Number XXXXX-XX-ENG

Version 2.6

November 2004

# Revision History

| Version | Primary Author(s) | Description of Version | Date Completed |
| --- | --- | --- | --- |
| 2.1 | Bill Dussell | Initial draft created for internal distribution and review comments. | 10/14/2004 |
| 2.2 | Bill Dussell | Added/Deleted Password fields to TrimTrac Application Protocol messages. Other minor edits. | 10/20/2004 |
| 2.3 | Bill Dussell | Add’l fields defined in REPORT_POS and STATUS_MSG | 10/23/2004 |
| 2.4 | Bill Dussell | Added Message Header Look-up Table | 10/27/2004 |
| 2.5 | Bill Dussell | Updated to Firmware 1.08 | 11/1/2004 |
| 2.6 | Bill Dussell | Added VAM Alert Wiring Diagram | 11/9/2004 |

Corporate Office

Trimble Navigation Limited

749 North Mary Avenue

Post Office Box 3642

Sunnyvale, CA 94088-3642 U.S.A.

Phone: +1-408-481-8940

1-800-545-7762

www.trimble.com

www.trimtrac.com

Copyright and Trademarks

© 1997–2004, Trimble Navigation Limited.

All rights reserved. Printed in the United States of America. Printed on recycled paper.

The Circle & Parallelogram and TrimTrac are trademarks of Trimble Navigation Limited. The Sextant logo, Globe & Triangle and Trimble are trademarks of Trimble Navigation Limited, registered in the United States Patent and Trademark Office. All other trademarks are the property of their respective owners.

Release Notice

This is November 2004 release (Revision 2.5) of the TrimTracTM Locator Technical Manual, Part Number XXXX-YY-ENG. The following limited warranties give you specific legal rights. You may have others, which vary from state/jurisdiction to state/jurisdiction.

Patents

US Patents 5877724, 6122506 and 6430503 apply.

Hardware Limited Warranty

Trimble warrants that this Trimble hardware product (the “Product”) shall be free from defects in materials and workmanship and will substantially conform to Trimble’s applicable published specifications for the Product for a period of one (1) year, starting from the date of delivery. The warranty set forth in this paragraph shall not apply to software/firmware products.

Software and Firmware License, Limited Warranty

This Trimble software and/or firmware product (the “Software”) is licensed and not sold. Its use is governed by the provisions of the applicable End User License Agreement (“EULA”), if any, included with the Software. In the absence of a separate EULA included with the Software providing different limited warranty terms, exclusions, and limitations, the following terms and conditions shall apply. Trimble warrants that this Trimble Software product will substantially conform to Trimble’s applicable published specifications for the Software for a period of ninety (90) days, starting from the date of delivery.

Warranty Remedies

Trimble's sole liability and your exclusive remedy under the warranties set forth above shall be, at Trimble’s option, to repair or replace any Product or Software that fails to conform to such warranty (“Nonconforming Product”), or refund the purchase price paid by you for any such Nonconforming Product, upon your return of any Nonconforming Product to Trimble in accordance with Trimble’s standard return material authorization procedures.

Warranty Exclusions and Disclaimer

These warranties shall be applied only in the event and to the extent that: (i) the Products and Software are properly and correctly installed, configured, interfaced, maintained, stored, and operated in accordance with Trimble's relevant operator's manual and specifications, and; (ii) the Products and Software are not modified or misused. The preceding warranties shall not apply to, and Trimble shall not be responsible for defects or performance problems resulting from (i) the combination or utilization of the Product or Software with products, information, data, systems or devices not made, supplied or specified by Trimble; (ii) the operation of the Product or Software under any specification other than, or in addition to, Trimble's standard specifications for its products; (iii) the unauthorized modification or use of the Product or Software; (iv) damage caused by accident, lightning or other electrical discharge, fresh or salt water immersion or spray; or (v) normal wear and tear on consumable parts (e.g., batteries).

THE WARRANTIES ABOVE STATE TRIMBLE'S ENTIRE LIABILITY, AND YOUR EXCLUSIVE REMEDIES, RELATING TO PERFORMANCE OF THE PRODUCTS AND SOFTWARE. EXCEPT AS OTHERWISE EXPRESSLY PROVIDED HEREIN, THE PRODUCTS, SOFTWARE, AND ACCOMPANYING DOCUMENTATION AND MATERIALS ARE PROVIDED “AS-IS” AND WITHOUT EXPRESS OR IMPLIED WARRANTY OF ANY KIND BY EITHER TRIMBLE NAVIGATION LIMITED OR ANYONE WHO HAS BEEN INVOLVED IN ITS CREATION, PRODUCTION, INSTALLATION, OR DISTRIBUTION INCLUDING, BUT NOT LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR PURPOSE, TITLE, AND NONINFRINGEMENT. THE STATED EXPRESS WARRANTIES ARE IN LIEU OF ALL OBLIGATIONS OR LIABILITIES ON THE PART OF TRIMBLE ARISING OUT OF, OR IN CONNECTION WITH, ANY PRODUCTS OR SOFTWARE. SOME STATES AND JURISDICTIONS DO NOT ALLOW LIMITATIONS ON DURATION OR THE EXCLUSION OF AN IMPLIED WARRANTY, SO THE ABOVE LIMITATION MAY NOT APPLY TO YOU. TRIMBLE NAVIGATION LIMITED IS NOT RESPONSIBLE FOR THE OPERATION OR FAILURE OF OPERATION OF GPS SATELLITES OR THE AVAILABILITY OF GPS SATELLITE SIGNALS.

Limitation of Liability

TRIMBLE’S ENTIRE LIABILITY UNDER ANY PROVISION HEREIN SHALL BE LIMITED TO THE GREATER OF THE AMOUNT PAID BY YOU FOR THE PRODUCT OR SOFTWARE LICENSE OR U.S.$25.00. TO THE MAXIMUM EXTENT PERMITTED BY APPLICABLE LAW, IN NO EVENT SHALL TRIMBLE OR ITS SUPPLIERS BE LIABLE FOR ANY INDIRECT, SPECIAL, INCIDENTAL OR CONSEQUENTIAL DAMAGES WHATSOEVER UNDER ANY CIRCUMSTANCE OR LEGAL THEORY RELATING IN ANY WAY TO THE PRODUCTS, SOFTWARE AND ACCOMPANYING DOCUMENTATION AND MATERIALS, (INCLUDING, WITHOUT LIMITATION, DAMAGES FOR LOSS OF BUSINESS PROFITS, BUSINESS INTERRUPTION, LOSS OF BUSINESS INFORMATION, OR ANY OTHER PECUNIARY LOSS), REGARDLESS WHETHER TRIMBLE HAS BEEN ADVISED OF THE POSSIBILITY OF ANY SUCH LOSS AND REGARDLESS OF THE COURSE OF DEALING WHICH DEVELOPS OR HAS DEVELOPED BETWEEN YOU AND TRIMBLE. BECAUSE SOME STATES AND JURISDICTIONS DO NOT ALLOW THE EXCLUSION OR LIMITATION OF LIABILITY FOR CONSEQUENTIAL OR INCIDENTAL DAMAGES, THE ABOVE LIMITATION MAY NOT APPLY TO YOU.

Notices

Class B Statement – Notice to Users. This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to Part 15 of the FCC rules. These limits are designed to provide reasonable protection against harmful interference in a residential installation. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instructions, may cause harmful interference to radio communication. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is

encouraged to try to correct the interference by one or more of the following measures:

- Reorient or relocate the receiving antenna.

- Increase the separation between the equipment and the receiver.

- Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

- Consult the dealer or an experienced radio/TV technician for help.

Changes and modifications not expressly approved by the manufacturer or registrant of this equipment can void your authority to operate this equipment under Federal Communications Commission rules.

Regulatory Approvals

CE

The TrimTrac Locator product complies with the essential requirements of the R&TTE Directive 199/5/EC as stated by the EC Declaration of Conformity (CE0681) and the EC R&TTE Type Examination Certificate. The TrimTrac Locator product complies with the European Telecommunications Standards Institute Specifications ETS300-342-1 (EMC for GSM 900MHZ and DCS 1800MHZ Radio Equipment and Systems).

EEC

The TrimTrac Locator product complies with Directive 72/245/EEC as amended by Directive 95/54/EC (el*72/245*95/54).

FCC The TrimTrac product complies with the FCC Part 15, FCC Part 24, and Industry Canada requirements. The TrimTrac product complies with Part 15 of the FCC rules. Operation is subject to the following two conditions: (1) This device may not cause harmful interference, and (2) This device must accept any interference received, including interference that may cause undesired operation.

FCC ID: JUPTRIMTRAC1

##### Contents

About this Manual	ix

Related Information	ix

Technical Assistance	x

Safety First	1

Simple Guidelines	1

Detailed Safety Information	2

Exposure to Radio Frequency Signals	2

Electronic Devices	2

Aircraft	3

Blasting Areas	3

Potentially Explosive Atmospheres	3

For Vehicles Equipped with an Air Bag	4

Specific Absorption Rates (SAR)	4

Overview	6

Introduction	6

TrimTrac Locator	6

Global System for Mobile Communications	8

Global Positioning System	10

TrimTrac Locator Defaults	11

Introduction	11

Security Considerations	11

Diagnostics	12

TrimTrac Locator Configuration	13

Introduction	13

Provisioning Mode and Equipment	13

Provisioning Set-up	13

Provisioning Commands	16

Use Guidelines	28

Introduction	28

General Guidelines	28

Theory of Operation	30

Introduction	30

Application State Machine Design Details	33

TrimTrac Application Protocol	40

Introduction	40

Message Format	40

TrimTrac Application Protocol Message Summary	43

TrimTrac Message Commands and Responses	44

TrimTrac Message Headers and Names	45

Configuration Messages	46

Query Messages	52

Position, Status and Response Messages	55

Technical Tips and Troubleshooting	62

Introduction	62

Specifications	68

Bibliography	69

Glossary	70

Basic Feature Parameter Ranges and Default Settings	72

Enhanced Feature Parameter Ranges and Default Settings	73

Vehicle Adapter Module Parameter Ranges and Default Settings	75

Read-Only Parameters, Formats and Ranges	76

##### List of Tables

Table 1, Diagnostic LED Blink Rates	12

Table 2, Summary of Provisioning Commands	16

Table 3, AT+CTKP Assignment	17

Table 4, AT+CTKP Query	17

Table 5, AT+CTKC Assignment	18

Table 6, AT+CTKC Query	19

Table 7, AT+CTKX Assignment	21

Table 8, AT+CTKX Query	23

Table 9, AT+CTKG Assignment	24

Table 10, AT+CTKG Query	24

Table 11, AT+CTKY Assignment	25

Table 12, AT+CTKY Query	26

Table 13, AT+CTK0 Query	27

Table 14, ATI Query	27

Table 15, Basic Message Format	41

Table 16, Message Qualifiers	41

Table 17, Sample XOR Checksum Source Code	42

Table 18, TrimTrac Application Protocol Messages	43

Table 19, TrimTrac Application Protocol Command/Response Summary	44

Table 20,  Message Header Look-up Table	45

Table 21, SET_ALERT_STATE Message	46

Table 22, SET_APP_CONFIG Message	47

Table 23, SET_EXT_APP_CONFIG Message	49

Table 24, SET_GPS_CONFIG Message	50

Table 25, SET_PROV_CONFIG Message	50

Table 26, SET_VAM_APP_CONFIG Message	51

Table 27, QUERY_CONFIG Message	52

Table 28, QUERY_LOG Message	53

Table 29, QUERY_POSITION Message	54

Table 30, REPORT_POS and STATUS_MSG Messages	56

Table 31, RESP_ALERT_STATE Message	57

Table 32, RESP_APP_CONFIG Message	57

Table 33, RESP_EXT_APP_CONFIG Message	59

Table 34, RESP_GPS_CONFIG Message	59

Table 35, RESP_PROV_CONFIG Message	60

Table 36, RESP_Query_AGGR Message	60

Table 37, RESP_QUERY_LOG Message	60

Table 38, RESP_VAM_APP Message	61

Table 39, Basic Feature Parameters and Defaults	72

Table 40, Enhanced Feature Parameters and Defaults.	74

Table 41, Enhanced Feature Parameters and Defaults.	75

Table 42, Read-only Parameters	76

##### List of Figures

Figure 1, Summary TrimTrac Operational State Diagram	31

Figure 2, VAM Alert Wiring Diagram	77

# About this Manual

Welcome to the TrimTracTM Locator Technical Manual. This manual is intended for use by system integrators, service providers and application developers (collectively, “Resellers”).  It is not intended for end-users of the TrimTrac locator.  Any end-user documentation is to be prepared and furnished by the Resellers.

This manual covers the TrimTrac locator with 1.05 and later firmware and operating on 900 MHz, 1800 MHz and 1900 MHz Global System for Mobile communication (GSM) networks. Data and Event Reporting support is by Short Message Service (SMS).  This manual describes how to set up, configure, install, operate, and troubleshoot the product. Even if you have used other GSM or Global Positioning System (GPS) products before, Trimble recommends that you spend some time reading this manual to learn about the special features of this product. If you are not familiar with GSM or GPS, visit Trimble Component Technologies’ Web site dedicated to the TrimTrac product (www.trimtrac.com) for a look at the device, GSM and GPS. Trimble assumes that you are familiar with Microsoft Windows (2000, XP), including HyperTerminal, and know how to use a mouse, select options from menus and dialogs, make selections from lists, and refer to online help.

This manual is available in portable document format (PDF) from the following Web site: http://www.trimtrac.com/support

## Related Information

Other sources of related information are:

TrimTrac Web site at www.trimtrac.com . This site is dedicated to TrimTrac locator.  Application notes, technical notes, and other useful product information are available from this site. These documents contain important information about software and hardware changes.

Release notes – the release notes describe new features of the product, information not included in the manuals, and any changes to the manuals. The release notes are available for download from the above Web address.

ftp.trimtrac.com – use the Trimble FTP site to send files or to receive files such as software patches, utilities, service bulletins, and FAQs. Alternatively, access the FTP site from the Trimble Web site: www.trimtrac.com/support.

## Technical Assistance

If you have a problem and cannot find the information you need in the product documentation, please contact your local Trimble Component Technologies sales office or sales engineer.  The technical support organization can be reached by telephone at  +44-1256-746-239 or, when dialing from within the United States, at 1-800-767-4822.

# Safety First

## Simple Guidelines

Please follow these guidelines when configuring or using the TrimTrac locator.  Violating these guidelines may be dangerous, illegal or otherwise detrimental.  Further detailed information is provided in this manual.

### Do Not Operate Where Prohibited

Do not allow the TrimTrac locator to operate wherever wireless phone use is prohibited or when doing so may cause interference or danger.  Examples include but are not limited to operation in hospitals, aircraft, near blasting sites or wherever operation can cause interference.

### Interference

Like all wireless devices, the TrimTrac locator may encounter electrical interference that may affect its performance.

### Avoid Body Contact with Device During Operation

Do not operate the TrimTrac locator in direct contact with your body.  Maintain minimum separation distance of 0.6 inch (15 mm) between the device and any parts of your body.

### Qualified Service

Except for batteries and Subscriber Identification Module (SIM) card, the TrimTrac contains no user serviceable or replaceable parts.  Non-functioning units must be returned to an authorized service center for repair or replacement.

### Accessories and Batteries

Use only approved accessories or batteries.  Do not connect incompatible products.  There is risk of explosion if batteries are replaced by an incorrect type.  Dispose of used batteries according to the instructions provided with the batteries.

### Water-Resistance

The TrimTrac locator is not waterproof.  Even though it is water-resistant, it is recommended that it be used where it is relatively dry and not subjected to either water streams or submersion.

# Detailed Safety Information

## Exposure to Radio Frequency Signals

The TrimTrac locator is a low power radio transmitter and receiver.  When it is ON, it receives and also sends out radio frequency (RF) signals.

In August 1996, the Federal Communications Commissions (FCC) adopted RF exposure guidelines with safety levels for hand-held wireless phones.  Those guidelines are consistent with safety standards previously set by both U.S. and international standards bodies:

ANSI C95.1 (1992)

NCRP Report 86 (1986)

ICNIRP (1996)

Those standards were based on comprehensive and periodic evaluations of the relevant scientific literature.  For example, over 120 scientists, engineers, and physicians from universities, government health agencies, and industry reviewed the available body of research to develop the ANSI Standard (C95.1)

While the TrimTrac locator is not intended for hand-held use, its design nonetheless complies with the FCC guidelines (and those standards).

## Electronic Devices

Most modern electronic equipment is shielded from RF signals.  However, certain electronic equipment may not be shielded against the RF signals generated by the TrimTrac locator.

### Pacemakers

The Health Industry Manufacturers Association recommends that a minimum separation of six (6”) inches be maintained between a handheld wireless phone and a pacemaker to avoid potential interference with the pacemaker.  These recommendations are consistent with the independent research by and recommendations of Wireless Technology Research.

Persons with pacemakers:

Should ALWAYS keep the TrimTrac locator more than eight inches from their pacemaker with the device is operational.

Should not carry the TrimTrac locator on their person

If there is any reason to suspect that interference is taking place, the TrimTrac locator battery pack should be removed immediately.

### Other Medical Devices

If any other personal medical devices are used in the vicinity of a TrimTrac locator, consult the manufacturers of the medical devices to determine if they are adequately shielded from external RF energy.  Physicians may be able to assist in obtaining this information.

Disable operation of the TrimTrac locator by removing the battery pack in health care facilities when any regulations posted in these areas prohibit the use of wireless phones or two-way radios.  Hospitals and health care facilities may be using equipment that could be sensitive to external RF energy.

### Vehicles

RF signals may affect improperly installed or inadequately shielded electronic systems in motor vehicles.  Check with the manufacturer or its representative regarding the vehicle.  Also consult the manufacturer of any equipment that has been added to the vehicle.

### Posted Facilities

Disable operation of the TrimTrac locator by removing the battery pack in any facility where posted notices prohibit the use of wireless phones or two-way radios.

## Aircraft

FCC regulations prohibit using wireless phones while in the air. Disable operation of the TrimTrac locator by removing the battery pack prior to boarding or loading in an aircraft

## Blasting Areas

To avoid interfering with blasting operations, disable operation of the TrimTrac locator by removing the battery pack when in a “blasting area” or in areas posted:  “Turn off two-way radio”.  Obey all signs and instructions.

## Potentially Explosive Atmospheres

Disable operation of the TrimTrac locator by removing the battery pack prior to entering any area with a potentially explosive atmosphere and obey all signs and instructions.  Sparks in such areas could cause an explosion or fire resulting in bodily injury or even death.

Areas with a potentially explosive atmosphere are often, but not always marked clearly.  Potential areas may include:  fueling areas (such as gasoline stations); below deck on boats; fuel or chemical transfer or storage facilities; vehicles using liquefied petroleum gas (such as propane or butane); areas where the air contains chemicals or particles (such as grain, dust, or metal powders); and any other area where it would normally be advisable to turn off motor vehicle engines.

## For Vehicles Equipped with an Air Bag

An air bag inflates with great force.  DO NOT place objects, including the TrimTrac locator, in the area over the air bag or in the air bag deployment area.  If in-vehicle wireless equipment is improperly installed and the air bag inflates, serious injury could result.

## Specific Absorption Rates (SAR)

THE TRIMTRAC LOCATOR MEETS CERTAIN GOVERNMENT REQUIREMENTS FOR EXPOSURE TO RADIO WAVES.

The TrimTrac locator is a radio transmitter and receiver.  It is designed and manufactured not to exceed the emissions limits from exposure to radio frequency (RF) energy set by the Federal Communications Commission of the U.S. government when used in accordance with the instructions set forth in this manual.  These limits are part of comprehensive guidelines and establish permitted levels of RF energy for the general population.  The guidelines are based on standards that were developed by independent scientific organization through periodic and thorough evaluation of scientific studies.  The standards include a substantial safety margin designed to assure the safety of all persons, regardless of age and health.

The exposure standard for wireless mobile phones employs a unit of measurement known as the Specific Absorption Rate, or SAR.  The SAR limit set by the FCC is 1.6W/kg.  Tests of SAR are conducted using standard operation positions specified by the FCC with the phone transmitting at its highest certified power level in all tested frequency bands.  Although the SAR is determined at the highest certified power level, the actual SAR level of the phone while operating can be well below the maximum value.  This is because the phone is designed to operate at multiple power levels so as to use only the power required to reach the network.  In general, the closer the device is to a wireless base station antenna, the lower the power output.

Before a phone is available for sale to the public, it must be tested and certified to the FCC that it does not exceed the limit established by the government-adopted requirement for safe exposure when used in accordance with manufacturer instructions.  The tests are performed in positions and locations (e.g. near or on the body) as required by the FCC for each model.  The SAR value for the TrimTrac locator is less than 1.6 W/kg measured at a minimum separation distance of 0.6 inch (15 mm).  The TrimTrac locator is not designed to be worn on a person’s body.

The FCC has granted an Equipment Authorization for the TrimTrac locator with all reported SAR levels evaluated as in compliance with the FCC RF guidelines for devices not worn on the body.  SAR information on the TrimTrac locator is on file with the FCC and can be found under the Display Grant section of http://www.fcc.gov/oet/fccid after searching on FCC ID: JUPTRIMTRAC1.

Additional information on Specific Absorption Rates (SAR) can be found on the Cellular Telecommunications & Internet Association (CTIA) Web site at http://www.phonefacts.net

# Overview

## Introduction

This manual covers the TrimTrac locator operating on 900 MHz, 1800 MHz and 1900 MHz GSM networks.  As used in this manual, the term GSM shall include any and all of these frequencies.

Regulatory Approvals CE The TrimTrac product complies with the essential requirements of the R&TTE Directive 199/5/EC as stated by the EC Declaration of Conformity (CE0681) and the EC R&TTE Type Examination Certificate. The TrimTrac product complies with the European Telecommunications Standards Institute Specifications ETS300-342-1 (EMC for GSM 900MHZ and DCS 1800MHZ Radio Equipment and Systems). EEC The TrimTrac product complies with Directive 72/245/EEC as amended by Directive 95/54/EC (el*72/245*95/54). 1.1.2 FCC The TrimTrac product complies with FCC Part 15, FCC Part 24, and Industry Canada requirements. The TrimTrac product complies with Part 15 of the FCC rules. Operation is subject to the following two conditions: This device may not cause harmful interference, and This device must accept any interference received, including interference that may cause undesired operation.

## TrimTrac Locator

The TrimTrac locator is housed in a single, compact enclosure that simplifies installation and leads to greater reliability. The standard TrimTrac locator has four end-user replaceable alkaline AA batteries and there are no external antennas or other external connections.  This package is a mobile communications and positioning system module ideally suited for high volume automotive and asset management applications requiring a low-cost, battery or externally powered tracking device.  It operates over the GSM cellular networks and allows simple, fast, and efficient transfer of information between a mobile asset and an application hosted either on a server or on an end-user PC.

### Standard Features

The TrimTrac locator integrates the following into a single package:

GSM 900/1800/1900 MHz modem

High-sensitivity, 12-channel GPS receiver

Internal GSM and GPS antennas

TrimTrac application firmware and other integrated functions

Password-protected data communications

Support for limited data logging of up to 128 position or status records for subsequent download

### Subscriber Identity Module (SIM)

You must install a SMS-enabled Subscriber Identity Module (SIM) that has been initialized by your GSM service provider.

### Optional Plug-In Modules

The following options are available as plug-in modules that replace the standard TrimTrac locator batteries:

Provisioning Module.  Allows configuration of the TrimTrac locator via a USB 2.0 connection to a PC

Vehicle Adapter Module.  Allows connection to an external 9-32 VDC power supply and provides three types of open/closed switch and wiring monitoring connections.

## Global System for Mobile Communications

Cellular mobile telephone systems are widely available throughout the world. However, because cellular mobile telephone systems are regulated at the national level, these systems are not generally compatible with each other. To resolve the dilemma of being able to communicate from almost anywhere, but only within your own system, the European telecommunications operators—the Conference of European Postal and Telecommunications Administration (CEPT)—designed a new mobile telephone network.

This network has evolved into GSM, and CEPT has turned over management of GSM to the European Technical Standards Institute (ETSI). GSM is the predominant mobile communications system throughout the world. Outside the United States, most GSM systems operate at 900 MHz, 1800 MHz or both and services provided by these networks are generally referred to as Digital Communication Services (DCS). The United States GSM system operates at 1900 MHz and is generally referred to as Personal Communication Service (PCS).

### GSM Cellular Phone System

The Global System for Mobile (GSM) protocol offers a variety of data services that allow users to send and receive data at rates of up to 9600 bps. Data can be delivered over ISDN, Packet Switched or Circuit Switched Data Networks (PSDN or CSDN) and via the Short Message Service (SMS). The TrimTrac locator uses SMS, which is a store-and-forward service for the bi-directional exchange of alphanumeric messages of up to 160 characters.

Architecture of the GSM network

Any asset tracking or management system on GSM consists of several distinct components. The TrimTrac locator is the mobile unit that is installed in the vehicle, equipment or other mobile asset and contains the Subscriber Identity Module (SIM). The SIM card contains a unique International Mobile Subscriber Identity (IMSI) number. This enables the network to identify the user and therefore allow the terminal to have access to specific, subscriber services.

The GSM system is made up of two sections:

The Base Station Subsystem that controls the radio link with the mobiles through local cells

The Network Subsystem that controls the switching of calls between the network users, mobile to mobile, and between mobile and fixed lines

The Network Subsystem stores all administrative information including the current cell being used by the mobile unit that allows call routing and the roaming ability of GSM. An important feature of GSM is this ability to move across international and network borders, a feature that is described as “roaming.” If arrangements have been made with the service provider, the SIM card will be enabled for roaming.

Mobile Station (MS)

  - The TrimTrac locator includes a radio transmitter and receiver.

  - Subscriber Identity Module (SIM) – an electronic card containing a computer chip. The chip contains the subscriber information and operating system parameters. SIMs provide authentication, encryption, information storage, and subscriber account protection services (including Personal Identity Number or PIN, and Pin Unblocking Key or PUK). GSM users can move the SIM from one TrimTrac locator to another.

Other network components (part of the GSM network)

  - Short Message Service Center (SMSC)

  - Delivers text messages (up to 160 characters) to GSM users.

### GSM Operational Overview

The TrimTrac locator operates in accordance with the state diagram more fully described in the Theory of Operation chapter beginning on page 30 of this manual.

Whenever the TrimTrac locator has a new position or status to report, it updates its Status Message.  The TrimTrac locator then enters the GSM Transmit State and automatically searches for a GSM network using a set of tables on the SIM card to determine which GSM network the phone should try to reach.

These tables are the Public Land Mobile Network (PLMN) tables and each GSM network has its own unique PLMN number. This number is the Mobile Country Code (MCC) and the Mobile Network Code (MNC), which are also the first numbers of the subscriber’s IMSI. (The IMSI is the MCC, plus the MNC, plus the Mobile Station Identification Number.) The PLMN table finds either the subscriber’s home network or a network that will allow service, and registers to the network consistent with the handset.

The responding network’s Mobile Switching Center (MSC) passes this request for service to the Visitor Location Register (VLR). If the VLR has information about this IMSI, then it passes the request to the authentication center. If the VLR cannot find any information on this IMSI, it must pass the request to the Home Location Register and get approval before passing on the request.

Once the VLR has approval to grant the request for service, it knows the user identity, what features are authorized, and the authentication codes. The VLR then passes the request back to the MSC for routing to destination address specified by the TrimTrac locator. If the destination address is a land-based number, the MSC passes the call to the Public Switched Telephone Network (PSTN) for connection. If the destination address is another mobile number, the MSC repeats the process described above to locate the number being dialed.

## Global Positioning System

The Global Positioning System (GPS) is a satellite-based navigation system operated and maintained by the U.S. Department of Defense. GPS consists of a constellation of 24 satellites providing worldwide, 24-hour, three-dimensional (3D) coverage. Although originally conceived for military needs, GPS has a broad array of civilian applications including timing, surveying, fleet management, marine, land, aviation, and vehicle navigation. GPS is the most accurate technology available for navigation. As a satellite-based system, GPS is immune from the limitations of land-based systems, which have limited coverage and whose accuracy varies with geographic location and, even under ideal conditions, cannot compare with GPS. By computing the distance to GPS satellites orbiting the earth, a GPS receiver can calculate an accurate position. This process is called satellite ranging. GPS receivers can also provide precise time, speed, and course measurements that are important for vehicle mobile positioning and communications applications.

### GPS Receiver

The TrimTrac locator includes an advanced GPS receiver, which provides the position, course, speed and time information required for mobile asset management applications. The TrimTrac locator’s GPS receiver features a twelve-channel digital signal processor (DSP) which operates at the GPS L1 frequency (1575.42 MHz) and processes the Coarse/Acquisition (C/A) code portion of the GPS signal. The RF and digital signal processing components of the GPS module are custom ASICs designed by Trimble.

# TrimTrac Locator Defaults

## Introduction

The following tables describe the factory default settings of the TrimTrac locator.  All such default settings can be changed to suit the particular application requirements.  While most of the settings can be configured or changed by sending the appropriate SMS text messages over the GSM network, non-default entries for certain fields such as the Unit Identification (ID) number, Security Password and SIM PIN can only be entered or changed while the device is connected to a PC using the Provisioning Module.  Please refer to the TrimTrac Application chapter beginning on page 40 for detailed descriptions of each TrimTrac state.

The TrimTrac locator comes from the factory without time being set and with no GPS almanac or location stored in memory.  As a consequence, it is important that when the TrimTrac locator is first activated that it be given sufficient time to calculate its first position fix and to collect a full almanac.  Please see additional instructions in Use Guidelines chapter beginning on page 28.

## Security Considerations

### Communication Security

The security of the TrimTrac locator supports Short Message Peer to Peer (SMPP) protocol, which allows the application server or wireless carrier to insert any originating address into the messages it sends to the TrimTrac locator.  To maintain the security of the TrimTrac locator it will only accept an incoming TrimTrac Application message if its Unit ID field matches its own Unit ID and the password field matches its password.  This will ensure that only the server application will be able to send commands to direct it to report to a different location or to start reporting at a different rate.

### Configuration Security

The configurable parameters are divided into two groups, the provisioning group and the read/write group.

The provisioning group includes parameters that are only read from once the TrimTrac locator enters normal usage.  They are set at either time of manufacturing or possibly time of provisioning.  Some are never written only read from.  The values such as the Unit ID and Firmware Version are written at time of manufacturing.  The Destination Address is written at time of provisioning or can be changed over the air using the SET_PROV_CONFIG message.  The battery status values are updated by the firmware and only read from by the user.

The read/write group includes operational parameters that are changed as a part of the normal operation of the TrimTrac locator.  Sending a TrimTrac Application message to the TrimTrac locator over the air could change all these values. Using these messages the server application can change the functionality of the TrimTrac locator.  The communication security methods will protect these values from being changed by an unauthorized user.

The SIM PIN is a feature of GSM SIMs that allows the owner of the SIM to put a lock on the SIM.  In order to use the account associated with the SIM, the user of the GSM device must provide the SIM PIN after SIM insertion or device power up.  The SIM PIN setting is stored in the firmware and is used if the SIM requests it.  If requested, the SIM PIN is used to attempt to unlock the SIM.  If the unlock fails, the SIM PIN is marked as having caused a failure and not retried until the user physically connects the TrimTrac locator to a Provisioning Module and issues a new AT command changing the SIM PIN.  This is to prevent the SIM from becoming unusable after 10 SIM PIN failures.  The SIM PIN cannot be read back once set.  It can only be overwritten.

## Diagnostics

When the Diagnostics Mode is enabled and set to 1 (LED) the LED on the TrimTrac locator will blink at different rates depending on the TrimTrac locator’s operational state.  If the TrimTrac locator is powered off the LED is off.  If the estimated battery life is below the threshold of 10% the LED is turned on continuously while the TrimTrac locator is operational and not blinked.  Only if the batteries are good will the blinking rates in Table 1 apply.

| TrimTrac State | Blink Rate | In Plain Words… |
| --- | --- | --- |
| IDLE | 250ms ON / 250 ms OFF | Rapid blinking or while in Vigilant Mode |
| FIX | 2000ms ON / 2000 ms OFF | Long On, Long Off |
| TRANSMIT | 200ms ON / 1800ms OFF | Short Blinks |
| QUERY | 1800ms ON / 200ms OFF | Long On, very short off time |
| DELAY | Always OFF | Unit powers Off in Delay state. |
| DELAY to IDLE | One 2000ms ON | One blink as unit transitions from DELAY to IDLE state |

Table 1, Diagnostic LED Blink Rates

# TrimTrac Locator Configuration

## Introduction

Configuration is the process of setting the operational and communication parameters of the TrimTrac locator.  Most, but not all, of these parameters can be set or changed over the air; however, certain non-default entries, such as the Unit Identification number, Security Password and SIM personal identification number (PIN), can only be entered or changed when the TrimTrac locator is connected to a PC via a Provisioning Module.

Personnel without prior configuration or provisioning experience should familiarize themselves with the TrimTrac operation and application characteristics as more fully described in the Theory of Operation chapter beginning on page 30.

## Provisioning Mode and Equipment

Before a new TrimTrac locator can be used for the first time, it must be properly configured.  This entails substituting the Battery Pack Module or other optional modules with a Provisioning Module and then connecting it to the USB 2.0 port on a Microsoft Windows (2000, XP)-based PC.  Use of USB 1.0 ports or hubs is not recommended.  Some laptop computers may not have enough power available on the USB port to power Provisioning Module, especially when the laptop is operating on batteries.  If laptop is used to provision the TrimTrac locator, it is best to have the laptop connected to AC power.

Microsoft’s HyperTerminal is then used as the primary programming interface to send the proper AT Commands.  The AT Commands are described in this section and must be used the first time the TrimTrac locator is provisioned.  Text fields need to be enclosed in quotation marks “_”.

## Provisioning Set-up

Before a TrimTrac Provisioning Module can be connected and used with an USB 2.0-equipped Microsoft Windows (2000, XP)-based PC, the appropriate USB 2.0 drivers and HyperTerminal program must be installed on the PC.

### FTDI Driver Loading

The Provisioning Module uses an USB 2.0 interface chip from Future Technology Devices International Ltd. (FTDI).  The easiest way for HyperTerminal to communicate with the Provisioning Module is to download and install the appropriate FTDI driver on the PC on which HyperTerminal will run.

These Windows (2000, XP) drivers are available from FTDI for download and use at:

www.ftdichip.com/FTWinDriver.htm

Select, download and install the VCP Driver for either Win'98 / ME / 2000 / XP (with enhanced BM series support) driver following the instructions provided on the Web site and with the driver.

### HyperTerminal

HyperTerminal is a standard program included in all current versions of Microsoft Windows (2000, XP) and can be typically found in the Communications directory under Accessories.  If HyperTerminal is not already installed on the Windows (2000, XP) PC that will be used to configure the TrimTrac locator, you will need to install it from your original Windows (2000, XP) CDs.

### Connecting the Devices

Once the FTDI USB 2.0 device driver and HyperTerminal program are installed on the PC, connect the TrimTrac locator and Provisioning Module to the PC USB 2.0 port as follows:

- Remove the TrimTrac battery pack from the base TrimTrac locator

- Install an active SMS-enabled SIM card in the base unit SIM card holder

- Insert Provisioning Module into base TrimTrac locator and secure it using screw provided.

- Connect the USB 2.0 Type-A Male end of the data cable to the Provisioning Module

- Connect the other USB 2.0 Type-A Male end of the cable to the PC USB 2.0 port.  (Note: if the PC sound is enabled, there may be an audible sound when the cable and Provisioning Module are connected to the PC.  This indicates that the USB port on the PC may not have sufficient power.)

### Beginning a Provisioning Session

To commence a provisioning session, you must start HyperTerminal in the following steps

- Start HyperTerminal from the Windows (2000, XP), Start, All Programs, Accessories, Communications menu.

- A “New Connection” panel will appear and enter “TrimTrac” for the New Connection Name and click “OK” button

- A “Connect Using” panel will appear and from the pull down menu select the Com port you designated as the USB 2.0 port when you installed the FTDI driver (commonly, COM4)

- On the next panel and under “Port Settings”, select the following from the pull down menus:

Bits Per Second:	115200

Data Bit		8

Parity			None

Stop Bits		1

Flow Control		None

Click “OK” when done.

- If you wish to view what you type on the HyperTerminal Screen, click on File, Properties, Settings, ASCII Settings and checkmark the “Echo Typed Characters Locally” box.  Click “OK” to close each panel.

- To check whether you have successfully connected the TrimTrac and Provisioning Module to HyperTerminal, type:

at+ctkc?

- Assuming the factory default configuration has not been previously changed, the following response should appear:

+ctkc:  43200,300,120,900,60,168,15,0,0,1,0

OK

- You are now ready to begin provisioning the TrimTrac locator(s) by typing the AT+commands described in the following sections.

- When complete, reinstall the battery pack with four “AA” batteries.

### Configuring Multiple Units

If multiple TrimTrac locators need to be configured, then you can send the units text files with the desired settings rather then typing individual AT+commands.  For instance, sending the following from a text file sets the TrimTrac locator to its default settings and confirms the final settings and firmware version number:

at+ctkp="00000000","","","00000000"

at+ctkp?

at+ctkc=43200,300,120,900,60,168,15,0,0,1,0

at+ctkc?

at+ctkg=5,120,60,10,5

at+ctkg?

Ati

To configure HyperTerminal to send text files to the TrimTrac locator, select Echo and set the line delay to 500 milliseconds from the HyperTerminal ASCII Setup panel under File, Properties, Settings.

To send a text file, select and open the desired text file from Transfer, Send Text File panel.

## Provisioning Commands

### Provisioning AT Command Summary

The following AT commands are used to provision and configure the TrimTrac locator via HyperTerminal when connected to the Provisioning Module.

| Command | Description | See Page |
| --- | --- | --- |
| AT+CTKP | Assigns Communication parameters | 17 |
| AT+CTKP? | Queries Communication parameters | 17 |
| AT+CTKC | Assigns Application parameters | 18 |
| AT+CTKC? | Queries Application parameters | 18 |
| AT+CTKX | Assigns Extended Application parameters | 21 |
| AT+CTKX? | Queries Extended Application parameters | 21 |
| AT+CTKG | Assigns GPS parameters | 24 |
| AT+CTKG? | Queries GPS parameters | 24 |
| AT+CTKY | Assign Vehicle Adapter Module parameters | 25 |
| AT+CTKY? | Queries Vehicle Adapter Module parameters | 25 |
| AT+CTKO? | Retrieves Logged Messages | 27 |
| ATI | Queries Firmware Version | 27 |

Table 3, Summary of Provisioning Commands

### AT+CTKP Application Provisioning

Prior to the TrimTrac locator being used for the first time, the application must be provisioned using this command.  The AT+CTKP command configures the Communication parameters.  This command is the only method to change the Unit ID, SIM PIN and Security Password.  It can query the current settings or change them to new values.

| AT+CTKP=<Unit ID>,<Destination Address>,<SIM PIN>,<Security Password> OK |
| --- |
| <Unit ID> | Always 8 alphanumeric characters, UPPER CASE ONLY. Must use quotation marks “_”. Default “00000000” |
| <Destination Address> | Maximum 24 characters including international dialing “+” sign and country code. Must be in quotation marks. Default <Empty> |
| <SIM PIN> | If used, must be between 4 and 8 digits. Must use quotation marks “_” Default <Empty> |
| <Security Password> | Always 8 alphanumeric characters, UPPER CASE ONLY. . Must use quotation marks “_” Default “00000000” |

Table 4, AT+CTKP Assignment

| AT+CTKP? +CTKP: <Unit ID>,<Destination Address >,<SIM PIN>,<Security Password> OK |
| --- |
| <Unit ID> | Always 8 alphanumeric characters, UPPER CASE ONLY |
| <Destination Address> | 24 characters including international dialing “+” sign and country code. |
| <SIM PIN> | If used, must be between 4 and 8 digits. |
| <Security Password> | “********” |

Table 5, AT+CTKP Query

Note that when the SIM PIN field and the Security Password fields are queried using either AT+commands or TrimTrac Application Protocol messages, they are shown masked out with the ‘*’ character to prevent theft of the information.

### AT+CTKC  Application Configuration

The AT+CTKC command is used to configure the Basic Read/Write parameters of the TrimTrac locator.  It can query the current settings or change them to new values.

| AT+CTKC=<IDLE Timeout, T1>,<FIX Timeout, T2>,<TRANSMIT Timeout, T3>,<DELAY Timeout, T4>,<QUERY Timeout, T5>,<Almanac Timeout, T6>,<IDLE Wakeup Motion Timeout, T7>,<Motion Report Flag>,<Report Delay Flag>,<Diagnostics Mode>,<Communication Mode> OK |
| --- |
| <IDLE Timeout, T1> | In seconds (10 – 999990). Default 43200 |
| <FIX Timeout, T2> | In seconds (10 – 3600). Default 300 |
| <TRANSMIT Timeout, T3> | In seconds (10 – 3600). Default 120 |
| <DELAY Timeout, T4> | In seconds (10 – 86400). Default 900 |
| <QUERY Timeout, T5> | In seconds (10 – 3600). Default 60 |
| <Almanac Timeout, T6> | In hours (10 – 990). Default 168 |
| <IDLE Wakeup Motion Timeout, T7> | In seconds (0 – 90). Note: T7 is used exclusively while in the IDLE state; however, it is superseded by Rolling Motion Window, T21, whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Timeout, T7, must always be set greater than or equal to IDLE Wakeup Motion Second Count; else unit may not exit IDLE state due to motion. Default 15 |
| <Motion Report Flag> | 0=None; 1=Report first motion before GPS fix. Default 0 |
| <Report Delay Flag> | 0=Transmit All Messages; 1=Transmit NO Messages; 2=Transmit Motion-related Messages-only; 3= Transmit IDLE Timeout, T1 Status Messages-only. Default 0 |
| <Diagnostics Mode> | 0= None; 1= LED. Default 1 |
| <Communication Mode> | 0= SMS; 1= Future. Default 0 |

Table 6, AT+CTKC Assignment

| AT+CTKC? +CTKC: <IDLE Timeout, T1>,<FIX Timeout, T2>,<TRANSMIT Timeout, T3>,<DELAY Timeout, T4>,<QUERY Timeout, T5>,<Almanac Timeout, T6>,<IDLE Wakeup Motion Timeout, T7>,<Motion Report Flag>,<Report Delay Flag>,<Diagnostics Mode>,<Communication Mode> OK |
| --- |
| <IDLE Timeout, T1> | In seconds (10 – 999990). Default 43200 |
| <FIX Timeout, T2> | In seconds (10 – 3600). Default 300 |
| <TRANSMIT Timeout, T3> | In seconds (10 – 3600). Default 120 |
| <DELAY Timeout, T4> | In seconds (10 – 86400). Default 900 |
| <QUERY Timeout, T5> | In seconds (10 – 3600). Default 60 |
| <Almanac Timeout, T6> | In hours (10 – 990). Default 168 |
| <IDLE Wakeup Motion Timeout, T7> | In seconds (0 – 90). Note: T7 is used exclusively while in the IDLE state; however, it is superseded by Rolling Motion Window, T21, whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Timeout, T7, must always be set greater than or equal to IDLE Wakeup Motion Second Count; else unit may not exit IDLE state due to motion. Default 15 |
| <Motion Report Flag> | 0=None; 1=Report first motion before GPS fix. Default 0 |
| <Report Delay Flag> | 0=Transmit All Messages; 1=Transmit NO Messages; 2=Transmit Motion-related Messages-only; 3= Transmit IDLE Timeout, T1 Status Messages-only. Default 0 |
| <Diagnostics Mode> | 0= None; 1= LED. Default 1 |
| <Communication Mode> | 0= SMS; 1= Future. Default 0 |

Table 7, AT+CTKC Query

### AT+CTKX  Extended Application Configuration

The AT+CTKX command is used to configure the enhanced Basic Read/Write parameters of the TrimTrac locator.  It can query the current settings or change them to new values.

| AT+CTKX=<Scheduled Reporting Mode>,<Scheduled Report Time, T18>,<DELAY State Query Mode>,<IDLE State Query Mode>,<IDLE Stationary Mode Wakeup, T19>,<IDLE Stationary Mode Query Timeout, T20>,<Query Hold Flag>,<DELAY State Extended Motion Detection>,<Position Report Transmit Attempts>,<Status Message Transmit Attempts>,<IDLE Wakeup Motion Second Count>,<Rolling Motion Window, T21>,<Rolling Motion Second Count>,<Motion Override> OK |
| --- |
| <Scheduled Reporting Mode> | 0=None; 1=Daily; 2=Weekly. Default 0 |
| <Scheduled Report Time, T18> | In Seconds (0-604799). Note: This is either the seconds into the day or into the week for the device to schedule a report when this feature is enabled. If Scheduled Reporting Mode is set “0=None”, then enter 0. Default 0 |
| <DELAY State Query Mode> | 0=Disabled; 1=Enabled. Note: If set to “1=Enabled”, the unit does not power off during Delay state. Default 0 |
| <IDLE State Query Mode> | 0=Disabled; 1=Stationary; 2=Vigilant. Default 0 |
| <IDLE Stationary Mode Wakeup, T19> | In Seconds (10-999990). Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to “1=Stationary”. Default 3600 |
| <IDLE Stationary Mode Query Timeout, T20> | In Seconds (0, 10-3600). Note: Determines how long the unit dwells in the QUERY state each time IDLE Stationary Mode Wakeup, T19, expires. A value of zero causes the QUERY Timeout, T5, value to be used. Default 60 |
| <Query Hold Flag> | 0=Disabled; 1=Enabled. Note: Unit attempts to reconnect to the GSM network if the connection is lost during the QUERY state prior to the expiration of QUERY Timeout, T5. Default 0 |
| <DELAY State Extended Motion Detection> | 0=Disabled; 1=Enabled. Note: Allows the unit to filter spurious motion detections in DELAY state when set to “1=Enabled”. The unit does not power off during DELAY state and power consumption will increase. Default 1 |
| <Position Report Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1 |
| <Status Message Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1 |
| <IDLE Wakeup Motion Second Count> | In Seconds (1-90). Note: This parameter is used only while IDLE Wakeup Motion Timeout, T7, is running. It is superseded by Rolling Motion Second Count whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Second Count must always be set equal to or less than IDLE Wakeup Motion Timeout, T7; else unit may not exit IDLE state due to motion. Default 1 |
| <Rolling Motion Window, T21> | In Seconds (1-90). Note: T21 applies in all states except IDLE and FIX; provided, however, that is also automatically enabled for IDLE state whenever IDLE State Query Mode is set “2=Vigilant” OR when IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: Rolling Motion Window, T21, must always be set equal to or greater than Rolling Motion Second Count; else the unit may not exit QUERY state. Default 20 |
| <Rolling Motion Second Count> | In Seconds (1-90). Note: This parameter is enabled only when Rolling Motion Window, T21, is active. Default 10 |
| <Motion Override> | 0=Normal; 1=Motion Always; 2=Motion Never. Note: Overrides the motion sensor if set to a value other than “0=Normal”. If set to “1=Motion” Always, then the state machine will override the motion sensor such that the unit operates as if motion is always present. If set to “2=Motion Never”, then the state machine will ignore all motion and never generate a fix until the configuration is changed or otherwise commanded to do so (see QUERY_POSITION message). Default 0 |

Table 8, AT+CTKX Assignment

| AT+CTKX? +CTKX: <Scheduled Reporting Mode>,<Scheduled Report Time, T18>,<DELAY State Query Mode>,<IDLE State Query Mode>,<IDLE Stationary Mode Wakeup, T19>,<IDLE Stationary Mode Query Timeout, T20>,<Query Hold Flag>,<DELAY State Extended Motion Detection>,<Position Report Transmit Attempts>,<Status Message Transmit Attempts>,<IDLE Wakeup Motion Second Count>,<Rolling Motion Window, T21>,<Rolling Motion Second Count>,<Motion Override> OK |
| --- |
| <Scheduled Reporting Mode> | 0=None; 1=Daily; 2=Weekly. Default 0 |
| <Scheduled Report Time, T18> | In Seconds (0-604799). Note: This is either the seconds into the day or into the week for the device to schedule a report when this feature is enabled. If Scheduled Reporting Mode is set “0=None”, then enter 0. Default 0 |
| <DELAY State Query Mode> | 0=Disabled; 1=Enabled. Note: If set to “1=Enabled”, the unit does not power off during Delay state. Default 0 |
| <IDLE State Query Mode> | 0=Disabled; 1=Stationary; 2=Vigilant. Default 0 |
| <IDLE Stationary Mode Wakeup, T19> | In Seconds (10-999990). Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to “1=Stationary”. Default 3600 |
| <IDLE Stationary Mode Query Timeout, T20> | In Seconds (0, 10-3600). Note: Determines how long the unit dwells in the QUERY state each time IDLE Stationary Mode Wakeup, T19, expires. A value of zero causes the QUERY Timeout, T5, value to be used. Default 60 |
| <Query Hold Flag> | 0=Disabled; 1=Enabled. Note: Unit attempts to reconnect to the GSM network if the connection is lost during the QUERY state prior to the expiration of QUERY Timeout, T5. Default 0 |
| <DELAY State Extended Motion Detection> | 0=Disabled; 1=Enabled. Note: Allows the unit to filter spurious motion detections in DELAY state when set to “1=Enabled”. The unit does not power off during DELAY state and power consumption will increase. Default 1 |
| <Position Report Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1 |
| <Status Message Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1 |
| <IDLE Wakeup Motion Second Count> | In Seconds (1-90). Note: This parameter is used only while IDLE Wakeup Motion Timeout, T7, is running. It is superseded by Rolling Motion Second Count whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Second Count must always be set equal to or less than IDLE Wakeup Motion Timeout, T7; else unit may not exit IDLE state due to motion. Default 1 |
| <Rolling Motion Window, T21> | In Seconds (1-90). Note: T21 applies in all states except IDLE and FIX; provided, however, that is also automatically enabled for IDLE state whenever IDLE State Query Mode is set “2=Vigilant” OR when IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: Rolling Motion Window, T21, must always be set equal to or greater than Rolling Motion Second Count; else the unit may not exit QUERY state. Default 20 |
| <Rolling Motion Second Count> | In Seconds (1-90). Note: This parameter is enabled only when Rolling Motion Window, T21, is active. Default 10 |
| <Motion Override> | 0=Normal; 1=Motion Always; 2=Motion Never. Note: Overrides the motion sensor if set to a value other than “0=Normal”. If set to “1=Motion” Always, then the state machine will override the motion sensor such that the unit operates as if motion is always present. If set to “2=Motion Never”, then the state machine will ignore all motion and never generate a fix until the configuration is changed or otherwise commanded to do so (see QUERY_POSITION message). Default 0 |

Table 9, AT+CTKX Query

### AT+CTKG  GPS Configure

The AT+CTKG command configures the GPS parameters.  This command mirrors the functionality of the over-the-air GPS_CONFIG message.  It can query the current settings or change them to new values.

| AT+CTKG=<GPS Elevation Mask>,<GPS PDOP Mask>,<GPS PDOP Switch>,<GPS Signal Level>,<GPS Dynamics Mode> OK |
| --- |
| <GPS Elevation Mask> | In degrees (0-30). Default 5 |
| <GPS PDOP Mask> | In tenths of PDOP (60 – 200). Default 120 |
| <GPS PDOP Switch> | In tenths of PDOP (40 – 120). Default 60 |
| <GPS Signal Level> | In tenths of AMUs (10 – 80). Default 10 |
| <GPS Dynamics Mode> | 5=Automobile; Default 5 |

Table 10, AT+CTKG Assignment

| AT+CTKG? +CTKG: <GPS Elevation Mask>,<GPS PDOP Mask>,<GPS PDOP Switch>,<GPS Signal Level>,<GPS Dynamics Mode> OK |
| --- |
| <GPS Elevation Mask> | In degrees (0-30). Default 5 |
| <GPS PDOP Mask> | In tenths of PDOP (60 – 200). Default 120 |
| <GPS PDOP Switch> | In tenths of PDOP (40 – 120). Default 60 |
| <GPS Signal Level> | In tenths of AMUs (10 – 80). Default 10 |
| <GPS Dynamics Mode> | 5=Automobile. Default 5 |

Table 11, AT+CTKG Query

### AT+CTKY  VAM-only Application Configuration

The AT+CTKY command configures the application parameters specific to the Vehicle Adapter Module.

| AT+CTKY=<HPA Idle Timeout, T11>,<MPA Idle Timeout, T12>,<HPA Delay Timeout, T13>,<MPA Delay Timeout, T14>,<HPA Transmit Timeout, T15>,<MPA Transmit Timeout, T16>,<HPA Query Timeout, T17>,<HPA Transmit Attempts>,<MPA Transmit Attempts>,<LPA Transmit Attempts>,<Ignore HPA>,<Ignore MPA>,<Ignore LPA> OK |
| --- |
| <HPA Idle Timeout, T11> | In Seconds (10-999990). Default 10 |
| <MPA Idle Timeout, T12> | In Seconds (10-999990). Default 10 |
| <HPA Delay Timeout, T13> | In Seconds (10-86400). Default 10 |
| <MPA Delay Timeout, T14> | In Seconds (10-86400). Default 10 |
| <HPA Transmit Timeout, T15> | 0=Infinity; Else in Seconds (10-999990). Default 0 |
| <MPA Transmit Timeout, T16> | 0=Infinity; Else in Seconds (10-999990). Default 120 |
| <HPA Query Timeout, T17> | In Seconds (10-3600). Default 60 |
| <HPA Transmit Attempts> | 0=Until T15 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <MPA Transmit Attempts> | 0=Until T16 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <LPA Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <Ignore HPA> | 0=Do NOT Ignore; 1=Ignore. Default 0 |
| <Ignore MPA> | 0=Do NOT Ignore; 1=Ignore . Default 0 |
| <Ignore LPA> | 0=Do NOT Ignore; 1=Ignore. Default 0 |

Table 12, AT+CTKY Assignment

| AT+CTKY? CTKY: <HPA Idle Timeout, T11>,<MPA Idle Timeout, T12>,<HPA Delay Timeout, T13>,<MPA Delay Timeout, T14>,<HPA Transmit Timeout, T15>,<MPA Transmit Timeout, T16>,<HPA Query Timeout, T17>,<HPA Transmit Attempts>,<MPA Transmit Attempts>,<LPA Transmit Attempts>,<Ignore HPA>,<Ignore MPA>,<Ignore LPA> OK |
| --- |
| <HPA Idle Timeout, T11> | In Seconds (10-999990). Default 10 |
| <MPA Idle Timeout, T12> | In Seconds (10-999990). Default 10 |
| <HPA Delay Timeout, T13> | In Seconds (10-86400). Default 10 |
| <MPA Delay Timeout, T14> | In Seconds (10-86400). Default 10 |
| <HPA Transmit Timeout, T15> | 0=Infinity; Else in Seconds (10-999990). Default 0 |
| <MPA Transmit Timeout, T16> | 0=Infinity; Else in Seconds (10-999990). Default 120 |
| <HPA Query Timeout, T17> | In Seconds (10-3600). Default 60 |
| <HPA Transmit Attempts> | 0=Until T15 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <MPA Transmit Attempts> | 0=Until T16 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <LPA Transmit Attempts> | 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 0 |
| <Ignore HPA> | 0=Do NOT Ignore; 1=Ignore. Default 0 |
| <Ignore MPA> | 0=Do NOT Ignore; 1=Ignore . Default 0 |
| <Ignore LPA> | 0=Do NOT Ignore; 1=Ignore. Default 0 |

Table 13, AT+CTKY Query

### AT+CTKO? Retrieve Message Log Command

The AT+CTKO? command will retrieve all messages stored in the log while in the service mode, in the order of protocol sequence number.

AT+CTKO?

+CTKO:

{message}

OK

Table 14, AT+CTK0 Query

Note:  When using AT+CTKO? in HyperTerminal, use the “Capture Text” command under the “Transfer” menu.  Otherwise, some messages may be partially truncated as they are retrieved from the TrimTrac locator.

### ATI Retrieve Firmware Version Command

The ATI command will retrieve the firmware version.  Note that no “?” mark is used in this query

ati

Trimble Navigation Ltd

TrimTrac (tm)

Revision: {message}

OK

Table 15, ATI Query

# Use Guidelines

## Introduction

The TrimTrac locator is a completely self-contained end-user device.  As such no specific installation is required.  There are no external connections required for antennas or power when used in its standard battery-powered configuration.  Like all GPS and wireless devices, the TrimTrac locator will work best where it can have a relatively unobstructed view of the sky and wireless base station antenna.  Nonetheless, the TrimTrac locator employs advanced GPS technology that increases its ability to acquire weak GPS signals.  This allows the device to be deployed in environments where traditional GPS receivers may not be able to determine location.

## General Guidelines

### Initial Use after Provisioning

The TrimTrac locator comes from the factory without current time being set and without GPS almanac or location stored in memory.  As a consequence, it is important that when the TrimTrac locator is first activated that it be given sufficient time to calculate its first position fix and to collect a complete GPS almanac.

After the TrimTrac locator has been configured per the instruction provided in the TrimTrac Locator Configuration chapter, it is recommended that the TrimTrac be powered up, using either batteries or a Vehicle Adapter Module, and the unit remaining stationary with a clear, unobstructed view of the sky.  This will allow the TrimTrac locator to calculate a position fix in the shortest possible time and allow it to collect a GPS almanac.  During this first session, the TrimTrac locator up to fifteen (15) minutes beyond the expiration of T2 time (default 300 seconds) before sending a SMS message.

### Placement and Orientation

Generally, the TrimTrac will perform best when used as close as possible to horizontal plane, preferably with reasonably unobstructed clearance around the unit.  Field tests indicate that the TrimTrac locator performs reasonably well when placed in the glove box or under the front passenger seat in many contemporary automobiles.  It should not be installed in the trunk of a vehicle unless it can be place near or under the rear window package shelf.  Try to avoid placing the unit where its view of the sky is obstructed by metal or surfaces coated with metallic paint or films.

### RF Jamming

The TrimTrac locator should be installed as far away as possible from transmitting antennas, including satellite communication, radar, VHF and cellular. These transmitters may emit jamming signals that interfere with the GPS receiver’s ability to track GPS satellite signals. Generally, the stronger the other transmitting device, the wider the distance required between antennas. For the TrimTrac locator, a minimum clearance of 45 cm (approximately 18 in.) from these transmitting devices is recommended.

### Mounting

The TrimTrac locator is provided with mounting tabs that can be used to secure the device to a flat surface using screws or similar fasteners.  In the event these mounting tabs are not to be used, they can be broken-off by working them back and forth.

### Environmental Conditions

The TrimTrac locater mounting location must not exceed the environmental specifications of the device.  For instance, it cannot be installed inside a vehicle’s engine compartment, wheel well, chassis or any other location in which the conditions can reasonably be expected to exceed the device environmental specifications.

### Exposure to RF Radiation

As noted in the Safety First and Detailed Safety Information chapters, on pages 1 and 2, respectively, the TrimTrac locator is not to be used in direct contact with the body.  A minimum separation distance of 0.6 inch (15 mm) must be maintained during operation.  The TrimTrac locator is not intended for body-worn applications.

### Interference with Other Devices

The TrimTrac locator includes a GSM modem that may interfere with other electronic systems, such as car stereos, when it is transmitting.  To avoid such interference, it is recommended that the TrimTrac locator not be placed in close proximity to any other electronic systems or devices.

### Batteries

The TrimTrac locator is designed to work with four standard AA alkaline batteries.  Insert the batteries with the positive and negative polarities as indicated on the battery pack label.  Do not reverse polarities or use non-alkaline AA batteries; otherwise, permanent damage to the TrimTrac locator may result or there may be a risk of explosion or fire.  Dispose of used batteries in accordance with the battery manufacturer instructions.

# Theory of Operation

## Introduction

The TrimTrac Application operates the device as a state machine.  This state machine is persistent over power cycles so when the unit wakes up from a programmed sleep period it will be aware of its current state and thus know what step to do next.

Valid Motion is defined as motion detected and filtered for T7 (the algorithm for motion filtering is implementation-specific and is not described here). The process of motion filtering will occur in a separate task that is always running. The output of this task will be a status that represents Valid Motion.  This allows for the T7 filtering to always be enabled, even during the TX, QUERY, and DELAY states.  The motion filtering algorithm will be separately configurable for two different periods.  The T7 timer will be used for IDLE wakeup filtering.  The Rolling Motion Window, T21, will be used after the state machine leaves the IDLE state.  The only time when the filtering will not be available will be when the unit powers off.

The state machine has two possible paths depending on the Motion Report Flag.  This flag determines if a Motion Report will be sent on the first motion wakeup after being in IDLE mode.  If true, the flag causes the state machine to produce a Status Report (Motion Report) when waking up from motion out of the IDLE sleep mode.  If a Motion Report is sent into the TX state it will return to the FIX state afterwards to get a GPS fix and continue normally.

Figure 1, Summary TrimTrac Operational State Diagram

The state machine transitions through these states based on external inputs (motion sensor), timeouts (RTC and simple wait periods), and as a result of completing defined actions (communicating to the server), as follows:

IDLE:	The TrimTrac device spends the majority of its time in the IDLE state.  Detection of Valid Motion results in a transition to the FIX state if the Motion Report Flag is not true.  If the Motion Report Flag is true then motion will cause a transition to STATUS. An IDLE timeout causes a transition to the STATUS state.  The programmable IDLE timeout T1 is stored as seconds and will be on the order of 12 to 48 hours. There are also operating modes that allow the device to run the communications protocol stack during the IDLE state to receive and process incoming messages.

FIX:	The device attempts to fix a position for a programmable time period T2.  If a fix is achieved, the position is read by the application, the RTC is updated, and the state transitions to the STATUS state with status of “new fix available”.  If no position fix is achieved within the timeout period the state transitions to the STATUS state with status of “no new fix”.  The programmable GPS fix timeout T2 is stored as seconds and will be on the order of 3 to 5 minutes.

STATUS:	The TrimTrac device retrieves the latest status information and then transitions to the TRANSMIT state with the status of “status message”.  The status information include battery condition, battery change events and other such information.

TRANSMIT:	The device attempts to transmit alert, position and/or status information to the server.  First, the latest status information is combined with the position information in a new application protocol message.  The message is then sent to the GSM protocol stack to attempt transmission.  If the Motion Report Flag is true and the message was a Motion Report Message then the state transitions back to the FIX state.  If the message was not a Motion Report Message then it does not transition to the FIX state, instead if the transmission was successful, the state transitions to the QUERY state.  If the transmission failed the state transitions to the DELAY state or IDLE state if the TriggerType was IDLE timeout.  The programmable transmission timeout T3 is stored in seconds and will be on the order of 1 to 5 minutes.

QUERY:	The device waits to receive any requests from the server for a programmable query time period T5.  If any requests are received, they are processed in order and responses are sent if requested.  After the query timeout occurs the device transitions to the DELAY state if the TriggerType was motion, or to IDLE state if the TriggerType was IDLE timeout.  The programmable Query timeout T5 is stored as seconds and will be on the order of 1 to 2 minutes.

DELAY:	The device disables the motion sensor wakeup and goes to sleep for a programmable Delay sleep time T4.  When the unit wakes up it transitions to the IDLE state by enabling the motion sensor and going back to sleep. The programmable Delay timeout T4 is stored as seconds and will be on the order of 10 to 20 minutes.

## Application State Machine Design Details

As seen in Figure 1 the application state machine has six states that represent the current operation of the device.  This section gives a detailed description of each of the states, what events trigger transitions from each state, and the processing that occurs within each state and its transitions.

There will be two status variable used along with the state of the state machine.  They will be the TriggerType and the ReportType.  The TriggerType variable can be IDLE_WAKEUP, MOTION_WAKEUP, ALERT_WAKEUP, QUERY_WAKEUP, or SCHEDULED_WAKEUP.

The ReportType variable can be either STATUS_MSG or REPORT_POS. There will be one flag each for Motion Indication and Position Aged. Position Aged is defined as Valid Motion since the most recent successful position fix.  The set/clear of these flags are described in the following individual states.

### Alert Handling

In the application, there will be four states for each of HPA/MPA/LPA: 0 = Normal, 1 = Alert, 2 = Sent, 3 = Ack. There will be one flag for Power Good, and one flag for Armed Status.

Application Task Interface

Receipt of HPA, if HPA state is 0, send HPA_INIT signal;

Receipt of MPA, if MPA state is 0 and  HPA state is 0 or 3, send MPA_INIT signal; if MPA state is 0 and  HPA state is 1 or 2, set MPA state to 1;

Receipt of LPA, set Armed Status; Receipt of Normal, clear Armed Status;

Receipt of Power Good, set/clear Power Good;

Receipt of Valid Motion, set Motion Indication and Position Aged; If Armed Status is set and both HPA and MPA states are 0 or 3, send LPA_INIT signal; If Armed Status is set and either HPA or MPA states is 1 or 2, set LPA state to 1;

General Alert signal handling

HPA_INIT: Set HPA state to 1 and pass on the signal to current state; Clean up current state, transition to STATUS.

MPA_INIT: Set MPA state to 1 and pass on the signal to current state; Clean up current state if not TRANSMIT, transition to STATUS; if current state is TRANSMIT complete the current state, subject to certain over-rides, and transition to STATUS.

LPA_INIT: Set LPA state to 1 and pass on the signal to current state; Clean up current state if not TRANSMIT, transition to STATUS; if current state is TRANSMIT complete the current state, subject to certain over-rides, and transition to STATUS.

Individual state Alert processing is executed when the application enters each state.

### The IDLE State

The IDLE State is the state that the device enters when it goes to sleep waiting for Motion Indication (MOTION Wakeup), expiration of T1 (IDLE Wakeup), or an Alert Wakeup. Any of these three Wakeup conditions will be responsible for waking and causing the unit to transition from IDLE.  While in the IDLE state all hardware is turned off except for the Motion Sensor Wakeup Logic and the RTC; provided, however, Extended Query During Idle is not set to either Stationary (“1”) or Vigilant mode (“2”); else the GSM hardware and software are also periodically or continuously active, respectively.

- When the unit enters the IDLE State it checks if the Motion Indication is set. If yes, it immediately transitions to the FIX State bypassing the other checks.

- When the unit enters the IDLE State and the Motion Indication is clear, it programs an IDLE timer to wakeup T1 seconds later and enables the Motion Sensor Wakeup.

- It then powers off all the hardware (except when Extended Query During Idle is in Vigilant mode) and waits for a motion or T1 wakeup.

- When the unit wakes up it will check which stimulus woke it up and set the TriggerType variable.

- If the TriggerType was the Motion Sensor, the state machine will wait for T7 seconds and then check for motion again. If Motion Indication is set, it will transition to the FIX State if the Motion Report Flag is not true.  If the Motion Report Flag is TRUE an internal flag called the Motion Report Indicator will be set to remember that a motion status report is being performed and the state will transition to the STATUS State.  If Motion Indication is clear after T7 seconds the unit will return to sleep.

- If the TriggerType was an IDLE Timeout, the state machine will transition to the STATUS State.

- In Vigilant mode, the unit does not power off. It remains in IDLE ready to receive messages from the sever. Upon receipt of any SMS messages, the unit transitions to the QUERY state to process any such received messages.

- In Stationary mode, the RTC timer is programmed to wakeup at the earlier of Stationary Mode Wakeup Period derived time or T1 timeout.  At the Stationary Mode Wakeup Period time, the unit wakes up and transitions to the QUERY state.  Should any SMS messages be received during this QUERY state, they are processed immediately and the unit operates in accordance with any instructions contained therein.  If no SMS messages are received during this QUERY state prior to expiration of the Stationary Mode Query Timeout, then the unit returns to IDLE state.

- If Scheduled Reporting Mode is enabled the RTC timer is programmed to wakeup at the earlier of Second Count for Scheduled Reporting derived time or T1 timeout; provided, however, that the Report Delay Flag shall not apply to reports generated as a consequence of the Scheduled Reporting Mode being enabled.

Alert processing:

If HPA is 1, go to STATUS; If HPA is 2, and if Position Aged is set, go to FIX; if Position Aged is clear, sleep for HPA Idle Timeout, T11;

If MPA is 1, go to STATUS; If MPA is 2, and if Position Aged is set, go to FIX; if Position Aged is clear, sleep for MPA Idle Timeout, T12;

If LPA is 1, go to STATUS;

If HPA_INIT/ MPA_INIT / LPA_INIT signal received, go to STATUS;

### The FIX State

The FIX State is the state where the GPS engine is running trying to get a fix.  While in this state the GPS hardware is turned on and the GSM radio hardware is turned off.

- When the unit enters the FIX State it enables the GPS hardware, sets a timer to the T2 value and starts the FirstGPS software engine.

- The application firmware configures the FirstGPS engine with any settings from GPS parameter storage.

- Then the application periodically checks the FirstGPS engine for the fix status.  If a fix is achieved then the position is extracted, the RTC is updated, and the ReportType variable is set to NEW_FIX.

- If either a position fix is achieved or the timer timeout occurs the unit transitions to the STATUS State after disabling the GPS engine and powering off the GPS hardware.  The GPS information is stored into the report structure to be used during the TRANSMIT state.   There will also be an algorithm to determine if the quality of the fix is good enough to use based on position type 2D vs. 3D.  If the device detects NVRAM was completely empty (which is the case for a first time boot ) or otherwise has an incomplete almanac it will stay in the FIX state to collect GPS almanac and ephemeris.

NOTE: There may be a special case where the device leaves the GPS engine running after a fix is achieved but before transitioning to the STATUS State.  It would do this to allow for the collection of up to date almanac and ephemeris data every T6 seconds which will be on the order of days.

Alert processing:

If HPA_INIT or MPA_INIT signal received, gracefully shutdown GPS engine, go to STATUS.

### The STATUS State

The STATUS State is where the state machine goes if the RTC timeout occurred in the IDLE state and also after the FIX state finishes.  While in this state both the GSM and GPS hardware is turned off.

- When the unit enters the STATUS State it retrieves the Battery status information and stores it in the report structure to be used during the TRANSMIT state.

- The Motion Indication is cleared. If a ‘Position Fix’ is successful, clear Position Aged.

- It then transitions to the TRANSMIT State.

### The TRANSMIT State

The TRANSMIT State is where the state machine tries to send the latest position and status information to the server.  During this state the GPS hardware is powered off and the GSM radio is powered on.

- When the unit enters the TRANSMIT State it enables the GSM radio hardware.

- It then starts a timer with the value T3 and starts the TTPCom GSM protocol stack.

- The unit gives the position and status information to the Application Protocol software which returns the protocol message to be sent.

- It then waits for the GSM protocol stack to report that it has registered on the network.

- If the GSM protocol stack asks for the SIM PIN and the value in Provisioning storage has not been used unsuccessfully then it will be tried.  If the value is rejected, it will be remembered so that it is not tried again until the value is changed via the AT provisioning command.

- Once it registers on the network, the unit will send the protocol message to the server and wait for conformation from the GSM protocol stack that it was sent.

- If either the T3 Timer expires or the message is successfully sent and the Motion Report Indicator is set then the state transitions to the FIX State after clearing the Motion Report Indicator.

- If the GSM protocol stack reports a successful sending of the message then the state machine transitions to the QUERY State.

- If the T3 Timer expires before the successful transmission occurs then the state machine transitions to the DELAY State if the TriggerType was from motion.  If the TriggerType was IDLE timeout then the state machine transitions to the IDLE state.

Alert processing:

If HPA/MPA is not 0, build HPA/MPA REPORT_POS message with Alert State filled; Append the most recent Position report  message from the message log to the message;

If LPA is not 0, build LPA REPORT_POS message with Alert State filled;

If HPA is 1, attempt sending HPA message for T15; if message sent successfully, set HPA to 2, go to QUERY;

If HPA is 2, attempt sending HPA message for T3; if successfully, go to QUERY;

If MPA is 1, attempt sending MPA message for T16; if message sent successfully, set MPA to 2, go to FIX if Position Aged is set, go to QUERY if Position Aged is clear;

If MPA is 2, attempt sending MPA message for T3; if successfully, go to QUERY;

If LPA is 1, attempt sending LPA message for T3; if message sent successfully, set LPA to 2, go to FIX;

If LPA is 2, attempt sending LPA message for T3; if successfully, go to QUERY;

If HPA_INIT signal received, go to IDLE;

If MPA_INIT / LPA_INIT signal received, finish TRANSMIT processing, then go to IDLE, ignoring internal Motion Report Indicator flag.

If specified number of attempts (N1 to N5) failed before T3 timeout, go to the DELAY State if the TriggerType was from motion. If the TriggerType was an IDLE timeout then the state machine transitions to the IDLE state.

### The QUERY State

The QUERY State is where the Application waits for incoming messages from the server.  During this state the GPS hardware is powered off and the GSM radio is powered on.

- When the unit enters the QUERY State it starts a timer with value T5.

- The application then waits until the timer expires or a message arrives.

- If a message arrives it is passed to the Application Protocol software which may return one or more messages to send in response to the query. If the Query Timeout, T5, changes due to a received message the new time is immediately adopted.

- For each of the responses the application sends them back to the server each time waiting for a conformation from the GSM protocol stack that it was sent.

- If the timer expires while the application is sending responses to the query it will continue to send the responses and accept new queries.

- When the timer has expired and there are no messages waiting to be sent then the state machine transitions to the DELAY State if the TriggerType was from motion.  If the TriggerType was a DELAY timeout then the state machine transitions to the IDLE state.

- If Query Hold Flag is set, the application stays in QUERY until the current QUERY state is terminated by the appropriate messages being received from the server application or upon receipt of either a HPA, MPA or LPA initiation, or expiration of T5.  Should connection to the GSM network be lost during QUERY, then the unit shall re-establish connection to the GSM network when coverage becomes available again.

- If Extended Query During Delay is enabled, the QUERY timeout is set to the minimum value of T5 (10 seconds).

Alert processing:

If HPA is 1, go to IDLE;

If HPA is 2, ignore all Server messages received before SET_ALERT_STATE; if Position Aged is set, stay at QUERY for T17, then go to IDLE;

If MPA is 1, go to IDLE;

If MPA is 2, ignore all Server messages received before SET_ALERT_STATE;

If LPA is 1, go to IDLE;

If LPA is 2, ignore all Server messages received before SET_ALERT_STATE;

If HPA_INIT/ MPA_INIT/ LPA_INIT signal received, go to IDLE;

If SET_ALERT_STATE received, set HPA/MPA/LPA state only if the state is 2 or 3.

### The DELAY State

The DELAY State is where the state machine sits after a wakeup cycle and ignores the Motion Sensor input.  This effectively restricts the unit from reporting no more often that the DELAY interval T4.

- If Extended Query During Delay is Disabled (set to “0”) when the unit enters the DELAY State it disables the TTPCom GSM protocol stack and turns off the GSM hardware.

- If Motion Indication is set to “1”, it then programs the RTC timer to wakeup T4 seconds later and disables the Motion Sensor Wakeup Logic. Next it powers off all the hardware except the RTC Wakeup Logic.

- For non-VAM unit with Extended Motion Detection During Delay disabled, it then programs the RTC timer to wakeup T4 seconds later and disables the Motion Sensor Wakeup Logic. Next it powers off all the hardware except the RTC Wakeup Logic.

- For non-VAM unit with Extended Motion Detection During Delay enabled or for VAM unit, it then starts a timer to wakeup T4 seconds later. (The unit continues to detect motion.)

- When it wakes up it transitions to the IDLE State.

- If Extended Query During Delay is enabled, the unit does not disable GSM protocol stack nor turn off GSM hardware. Instead, it continues receiving messages from the GSM network. Upon receipt of any SMS message, the unit returns to the QUERY state to immediately process any such messages.

- If Scheduled Reporting Mode is enabled, a timer is programmed to go to IDLE state at the earlier of the Second Count for Scheduled Reporting derived time or T4 timeout.

Alert processing:

If HPA is 1, go to IDLE;

If HPA is 2, if Position Aged is set, go to IDLE; if Position Aged is clear, sleep for T13;

If MPA is 1, go to IDLE;

If MPA is 2, if Position Aged is set, go to IDLE; if Position Aged is clear, sleep for T14;

If LPA is 1 or Armed Status is set, go to IDLE

If HPA_INIT/MPA_INIT/LPA_INIT signal received, go to IDLE

# TrimTrac Application Protocol

## Introduction

The TrimTrac Application Protocol is used to communicate with and control TrimTrac locators that have already been provisioned and deployed to the field.

The TrimTrac locator communicates with the server application by sending and receiving SMS messages based on an ASCII-like protocol (in lieu of the AT+commands used during initial provisioning).  This TrimTrac Application Protocol uses the same message structure as the Trimble ASCII Interface Protocol (TAIP) even though no TAIP messages defined for Trimble products other than the TrimTrac locator are used.  It is used to communicate with and control TrimTrac locators that have already been provisioned and deployed to the field.

For security reasons, the only parameters that cannot be changed over-the-air using the TrimTrac Application Protocol are the Unit Identification number, SIM PIN and Security Password.

## Message Format

### Basic Message

All TrimTrac Application Protocol messages use printable ASCII characters. Upper case and lower case alpha characters are generally interchangeable, i.e., lower case characters are converted to upper case alpha in the TrimTrac locator before parsing.

Each message has the following general format with the contents of the data string being message dependant.  Valid messages are limited to 128 characters.

>ABB{C}[;PW=PPPPPPPP];ID=YYYYYYYY;*ZZ<

| Element | Meaning |
| --- | --- |
| > | Start of new message |
| < | End of message |
| A | Message Qualifier (Q, R, or S) |
| BB | 2-character Message Identifier (Must be TK) |
| C | Data string. |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY. Default 00000000 |
| ZZ | 2-character checksum. |
| {x} | Signifies that x can occur zero or more times |
| [x] | Signifies that x may optionally occur once |

Table 16, Basic Message Format

### Message Framing

Each TrimTrac Application Protocol message is framed by the start, end ASCII characters ‘>’, ‘<’, respectively. These characters are not allowed other than as start-of-message and end-of-message indicators.

### Message Qualifiers

A one-character Message Qualifier is used to describe the action to be taken on the message. The following table lists the valid qualifiers:

| Qualifier | Action |
| --- | --- |
| Q | Query for data or parameters (sent to TrimTrac locator) |
| S | Set or configure parameters (sent to TrimTrac locator) |
| R | Response to a query or a scheduled or autonomous report (from the TrimTrac locator) |

Table 17, Message Qualifiers

### Data String

The Message Qualifier and the Message Identifier dictate the format and length of the data string. The Data String can consist of any printable ASCII characters with the exception of the > and < characters. Most messages are length sensitive and many use the ‘;’ character as field separator.  Data fields are fixed length regardless of the values entered.

### Security Password

A Security Password (denoted as “PW” in messages) must be used in all communications with the TrimTrac locator. The default Security Password is set to “00000000”; however, the TrimTrac locator may be assigned any numeric password of up to eight characters while the TrimTrac locator is connected to a Provisioning Module.

The TrimTrac locator checks all incoming messages for a Security Password and all incoming message must include a Security Password. If the Security Password included in a message sent to TrimTrac locator does not match the Security Password configured in the TrimTrac device, then the message is ignored.

### Unit ID

The Unit ID must be used in all communications with the TrimTrac locator. The TrimTrac locator may be assigned a numeric Unit ID of eight digits only while the TrimTrac locator is connected to a Provisioning Module (available separately).  The default Unit ID is set to 00000000.

The TrimTrac locator checks all incoming messages for a Unit ID and all incoming message must include a Unit ID. If the Unit ID included in a message sent to TrimTrac locator does not match the Unit ID configured in the TrimTrac device, then the message is ignored.

### Checksum

The checksum field is always required and provides for a two-digit hexadecimal checksum value, which is computed by XOR’ing all characters from the beginning of the message up to and including the * character. See Table 18, Sample XOR Checksum Source Code. The checksum is always the last element of the message before the end-of-message delimiter.

/******************************************************************************* * Function: AppProtocolCalcTAIPChecksum * Parameters: pszTAIPMsg, checksum * Returns: Pointer to Checksum Header ;* if found, NULL otherwise. * Description: This function checks for the presense of the TAIP checksum * header. If it exists it calculates the checksum and * places it in the checksum parameter and returns a pointer * to the checksum header. * Otherwise it returns NULL without changing checksum. ******************************************************************************/ char* AppProtocolCalcTAIPChecksum(char *pszTAIPMsg, unsigned char *checksum) { char *pcEnd; char *pc; unsigned char cs; if((pcEnd = strstr(pszTAIPMsg, ";*")) != NULL) { pc = pszTAIPMsg; // Start of the checsumed chars. pcEnd += 2; // Move to the first non-checksumed char. cs = 0; while(pc < pcEnd) { cs ^= *pc; pc++; } *checksum = cs; return pcEnd-2; } else { return NULL; } }

Table 18, Sample XOR Checksum Source Code

## TrimTrac Application Protocol Message Summary

The following over-the-air TrimTrac Application Protocol Messages are used to communicate with and control the TrimTrac locator.

| Message | Description | See Page |
| --- | --- | --- |
| QUERY_CONFIG | Requests current Application, Communication or GPS parameters | 52 |
| QUERY_LOG | Requests logged messages (REPORT_POS and STATUS_MSG) by Report Sequence Number | 53 |
| QUERY_POSITION | Requests current or logged position information | 54 |
| REPORT_POS | Basic position message | 55 |
| RESP_ALERT_STATE | Confirms SET_ALERT_STATE message receipt and processing | 57 |
| RESP_APP_CONFIG | Reports current Basic Application parameters | 57 |
| RESP_EXT_APP_CONFIG | Reports current Extended Application parameters | 59 |
| RESP_GPS_CONFIG | Reports current GPS parameters | 58 |
| RESP_PROV_CONFIG | Reports current Communication parameters | 60 |
| RESP_QUERY_AGGR | Reports summary of two logged messages | 60 |
| RESP_QUERY_LOG | Reports requested logged messages by Report Sequence Number | 60 |
| RESP_VAM_APP_CONFIG | Reports current VAM application parameters | 61 |
| SET_ALERT_STATE | Acknowledges or clears VAM alerts | 46 |
| SET_APP_CONFIG | Changes Basic Application parameters | 47 |
| SET_EXT_APP_CONFIG | Changes Extended Application parameters | 49 |
| SET_GPS_CONFIG | Changes GPS parameters | 50 |
| SET_PROV_CONFIG | Changes Communication parameters | 50 |
| SET_VAM_APP_CONFIG | Changes VAM application paramaters | 51 |
| STATUS_MSG | Same as REPORT_POS except no location/velocity data | 55 |

Table 20, TrimTrac Application Protocol Messages

## TrimTrac Message Commands and Responses

| Command | Response |
| --- | --- |
| SET_APP_CONFIG (Page 47) | RESP_APP_CONFIG (Page 57) |
| SET_EXT_APP_CONFIG (Page 49) | RESP_EXT_APP_CONFIG (Page 59) |
| SET_PROV_CONFIG (Page 50) | RESP_PROV_CONFIG (Page 60) |
| SET_GPS_CONFIG (Page 50) | RESP_GPS_CONFIG (Page 58) |
| QUERY_CONFIG (Page 52) | RESP_APP_CONFIG (Page 57) |
| QUERY_LOG (Page 53) | RESP_QUERY_LOG (Page 60) or RESP_QUERY_AGGR (Page 60) |
| QUERY_POSITION (Page 54) | REPORT_POS or STATUS_MSG and REPORT_POS (Page 55) |
| SET_VAM_APP_CONFIG (Page 51) | RESP_VAM_APP_CONFIG (Page 61) |
| SET_ALERT_STATE (Page 46) | RESP_ALERT_STATE (Page 57) |

Table 21, TrimTrac Application Protocol Command/Response Summary

## TrimTrac Message Headers and Names

| Message Header | Message Name | See Page |
| --- | --- | --- |
| >QTKA | QUERY_CONFIG (APPLICATION) | 52 |
| >QTKD | QUERY_POSITION | 54 |
| >QTKG | QUERY_CONFIG (GPS) | 52 |
| >QTKR | QUERY_LOG | 53 |
| >QTKV | QUERY_CONFIG (PROVISIONING) | 52 |
| >RTK{1-4} | RESP_QUERY_AGGR | 60 |
| >RTKA | RESP_APP_CONFIG | 57 |
| >RTKG | RESP_GPS_CONFIG | 58 |
| >RTKL | RESP_ALERT_STATE | 57 |
| >RTKP | REPORT_POS | 55 |
| >RTKR | RESP_QUERY_LOG | 60 |
| >RTKS | STATUS_MSG | 55 |
| >RTKV | RESP_PROV_CONFIG | 60 |
| >RTKX | RESP_EXT_APP_CONFIG | 59 |
| >RTKY | RESP_VAM_APP | 61 |
| >STKA | SET_APP_CONFIG | 47 |
| >STKG | SET_GPS_CONFIG | 50 |
| >STKL | SET_ALERT_STATE | 46 |
| >STKV | SET_PROV_CONFIG | 50 |
| >STKX | SET_EXT_APP_CONFIG | 49 |
| >STKY | SET_VAM_APP_CONFIG | 51 |

Table 22,  Message Header Look-up Table

## Configuration Messages

The following messages are sent to the TrimTrac locator to configure application, GPS and GSM parameters and to set Vehicle Adapter Module alert and application parameters.

### SET_ALERT_STATE

This message is sent to the TrimTrac locator to acknowledge or clear alert states.

| >STKABCD;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | Always ‘L’: Indicates alert state setting |
| B | HPA state: ‘X’ = Do not care, ‘3’ = Ack, ‘0’ = Clear |
| C | MPA state: ‘X’ = Do not care, ‘3’ = Ack, ‘0’ = Clear |
| D | LPA state: ‘X’ = Do not care, ‘3’ = Ack, ‘0’ = Clear |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 23, SET_ALERT_STATE Message

### SET_APP_CONFIG

The SET_APP_CONFIG message is used by the server application to set the TrimTrac Application parameters in the TrimTrac locator.  When received the TrimTrac locator will send a RESP_APP_CONFIG message in response.

| >STKABBBBBBCCCCCCDDDDDDEEEEEEFFFFFFGGGTTHIJK;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘A’ = Application Parameters |
| BBBBBB | IDLE Timeout, T1. In seconds (10 – 999990). Default 43200 |
| CCCCCC | FIX Timeout, T2. In seconds (10 – 3600). Default 300 |
| DDDDDD | TRANSMIT Timeout, T3. In seconds (10 – 3600). Default 120 |
| EEEEEE | DELAY Timeout, T4. In seconds (10 – 86400). Default 900 |
| FFFFFF | QUERY Timeout, T5. In seconds (10 – 3600). Default 60 |
| GGG | Almanac Timeout, T6. In hours (10 – 990). Default 168 |
| TT | IDLE Wakeup Motion Timeout, T7. In seconds (0 – 90). Note: T7 is used exclusively while in the IDLE state; however, it is superseded by Rolling Motion Window, T21, whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Timeout, T7, must always be set greater than or equal to IDLE Wakeup Motion Second Count; else unit may not exit IDLE state due to motion. Default 15 |
| H | Motion Report Flag. 0=None; 1=Report first motion before GPS fix. Default 0 |
| I | Report Delay Flag. 0=Transmit All Messages; 1=Transmit NO Messages; 2=Transmit Motion-related Messages-only; 3= Transmit IDLE Timeout, T1 Status Messages-only. Default 0 |
| J | Diagnostics Mode. 0= None; 1= LED. Default 1 |
| K | Communication Mode. 0= SMS; 1= Future. Default 0 |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 24, SET_APP_CONFIG Message

### SET_EXT_APP_CONFIG

This message is used to set the Extended Application parameters in the TrimTrac device.  When received the TrimTrac device will send a RESP_EXT_APP_CONFIG message in response.

| >STKABCCCCCCDEFFFFFFGGGGGGHIJJJKKKLLMMNNO;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘X’ = Extended Application Parameters |
| B | Scheduled Reporting Mode. 0=None; 1=Daily; 2=Weekly |
| CCCCCC | Scheduled Report Time, T18. In Seconds (0-604799). Note: This is either the seconds into the day or into the week for the device to schedule a report when this feature is enabled. If Scheduled Reporting Mode is set “0=None”, then enter 0. Default 0. |
| D | DELAY State Query Mode. 0=Disabled; 1=Enabled. Note: If set to “1=Enabled”, the unit does not power off during Delay state. Default 0 |
| E | IDLE State Query Mode. 0=Disabled; 1=Stationary; 2=Vigilant. Default 0. Note: DELAY State Query Mode is treated as always 1=Enabled when IDLE State Query Mode is set to 2=Vigilant. |
| FFFFFF | IDLE Stationary Mode Wakeup, T19. In Seconds (10-999990). Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to “1=Stationary”. Default 3600. |
| GGGGGG | IDLE Stationary Mode Query Timeout, T20. In Seconds (0, 10-3600). Note: Determines how long the unit dwells in the QUERY state each time IDLE Stationary Mode Wakeup, T19, expires. A value of zero causes the QUERY Timeout, T5, value to be used. Default 60. |
| H | Query Hold Flag. 0=Disabled; 1=Enabled. Note: Unit attempts to reconnect to the GSM network if the connection is lost during the QUERY state prior to the expiration of QUERY Timeout, T5. Default 0. |
| I | DELAY State Extended Motion Detection. 0=Disabled; 1=Enabled. Note: Allows the unit to filter spurious motion detections in DELAY state when set to “1=Enabled”. The unit does not power off during DELAY state and power consumption will increase. Default 1. |
| JJJ | Position Report Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1. |
| KKK | Status Message Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 1. |
| LL | IDLE Wakeup Motion Second Count. In Seconds (1-90). Note: This parameter is used only while IDLE Wakeup Motion Timeout, T7, is running. It is superseded by Rolling Motion Second Count whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Second Count must always be set equal to or less than IDLE Wakeup Motion Timeout, T7; else unit may not exit IDLE state due to motion. Default 1. |
| MM | Rolling Motion Window, T21. In Seconds (1-90). Note: T21 applies in all states except IDLE and FIX; provided, however, that is also automatically enabled for IDLE state whenever IDLE State Query Mode is set “2=Vigilant” OR when IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: Rolling Motion Window, T21, must always be set equal to or greater than Rolling Motion Second Count; else the unit may not exit QUERY state. Default 20. |
| NN | Rolling Motion Second Count. In Seconds (1-90). Note: This parameter is enabled only when Rolling Motion Window, T21, is active. Default 10. |
| O | Motion Override. 0=Normal; 1=Motion Always; 2=Motion Never. Note: Overrides the motion sensor if set to a value other than “0=Normal”. If set to “1=Motion” Always, then the state machine will override the motion sensor such that the unit operates as if motion is always present. If set to “2=Motion Never”, then the state machine will ignore all motion and never generate a fix until the configuration is changed or otherwise commanded to do so (see QUERY_POSITION message). Default 0. |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 25, SET_EXT_APP_CONFIG Message

### SET_GPS_CONFIG

The SET_GPS_CONFIG message is used by the server application to set the TrimTrac GPS parameter values in the TrimTrac locator.  When received the TrimTrac locator will send a RESP_GPS_CONFIG message in response.  Please note that these GPS configuration parameters will seldom need to be changed from default values.  It is NOT recommended that they be changed without first consulting with your Trimble representative.

| >STKABBCCCDDDEEEF;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘G’ = GPS Parameters |
| BB | GPS Elevation Mask. In degrees (0-30). Default 5 |
| CCC | GPS PDOP Mask. In tenths of PDOP (60 – 200). Default 120 |
| DDD | GPS PDOP Switch. In tenths of PDOP (40 – 120). Default 60 |
| EEE | GPS Signal Level. In tenths of AMUs (10 – 80). Default 10 |
| F | GPS Dynamics Mode. 5=Automobile. Default 5 |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 26, SET_GPS_CONFIG Message

### SET_PROV_CONFIG

The SET_PROV_CONFIG message is used by the server application to set the Communication values in the TrimTrac locator.  When received by the TrimTrac locator, the unit will send a RESP_PROV_CONFIG message in response.

| >STKABBBBBBBBBBBBBBBBBBBBBBBB;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘V’ = Application Provisioning Parameters |
| BBBBBB BBBBBB BBBBBB BBBBBB | Destination Address. 24 characters including international dialing “+” sign and country code. Field padding is in spaces before the international dialing “+” sign. Default <Empty>. |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 27, SET_PROV_CONFIG Message

### SET_VAM_APP_CONFIG

This message will be used by the server to set the VAM-only Application Parameter Values in the TrimTrac device.  When received the TrimTrac device will send a RESP_VAM_APP_CONFIG message in response. The message is ignored by TrimTrac locators not equipped with a VAM.

| >STKABBBBBBCCCCCCDDDDDDEEEEEEFFFFFFGGGGGGHHHHHHIIIJJJKKKLMN;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | VAM-only Configuration Set: ‘Y’ = VAM-only Parameters |
| BBBBBB | HPA Idle Timeout, T11. In Seconds (10-999990) Default 10 |
| CCCCCC | MPA Idle Timeout, T12. In Seconds (10-999990). Default 10 |
| DDDDDD | HPA Delay Timeout, T13. In Seconds (10-86400). Default 10 |
| EEEEEE | MPA Delay Timeout, T14. In Seconds (10-86400). Default 10 |
| FFFFFF | HPA Transmit Timeout, T15. 0=Infinity; Else in Seconds (10-999990). Default 0 |
| GGGGGG | MPA Transmit Timeout, T16. 0=Infinity; Else in Seconds (10-999990). Default 120 |
| HHHHHH | HPA Query Timeout, T17. In Seconds (10-3600). Default 60 |
| III | HPA Transmit Attempts. 0=Until T15 Expires; 1-255=Number of Tx Attempts. Default 0. |
| JJJ | MPA Transmit Attempts. 0=Until T16 Expires; 1-255=Number of Tx Attempts. Default 0 |
| KKK | LPA Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts. Default 0 |
| L | Ignore HPA. 0=Do NOT Ignore; 1=Ignore. Default 0 |
| M | Ignore MPA. 0=Do NOT Ignore; 1=Ignore . Default 0 |
| N | Ignore LPA. 0=Do NOT Ignore; 1=Ignore. 0 |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 28, SET_VAM_APP_CONFIG Message

## Query Messages

### QUERY_CONFIG

This QUERY_CONFIG message is used by the server application to request the TrimTrac locator send its TrimTrac Application, GPS or Communication parameters in the appropriate RESP_APP_CONFIG, RESP_PROV_CONFIG or RESP_GPS_CONFIG message.

| >QTKA;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘G’ = GPS Parameters ‘A’ = Application Parameters ‘V’ = Provisioning Parameters |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 29, QUERY_CONFIG Message

### QUERY_LOG

This message is used by the server application to request Report Sequence Number past REPORT_POS or STATUS_MSG messages that may not have been received at the server application.  The TrimTrac locator will send the corresponding messages to the server application in response to this message at the rate of REPORT_POS or STATUS_MSG per message.  At the end of the messages a RESP_QUERY_LOG or RESP_QUERY_AGGR is sent.

| >QTKABBBBCCCC[DE[FGHIJJJK[LLLLMMMMMM[NNNNOOOOOO]]]];PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | Always ‘R’: Indicates a query for old REPORT messages |
| BBBB | Beginning Protocol Sequence Number. 16-bit Hex (0000-FFFF) incrementing by 1 for each logged report. |
| CCCC | Ending Protocol Sequence Number. 16-bit Hex (0000-FFFF) incrementing by 1 for each logged report |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |
| Optional |  |
| D | Aggregate Log Reporting Flag: ‘T’ = enabled, ‘F’ = disabled. When enabled, aggregate reports may be returned. |
| E | Stop RESP_QUERY_LOG message from being sent: ‘T’ = do not send, ‘F’ = send. Used to stop the unit from fulfilling previous QUERY_LOG requests. |
| F | Filter 1: 'Z' = All, 'U' = Unsent only. |
| G | Filter 2: 'Z' = All, 'P' = Position only, 'S' = Status only. |
| H | Filter 3: 'Z' = All, 'A' = Alert only |
| I | Time range: 'Z' = Unused, 'N' = Newest, 'O' = Oldest |
| JJJ | Maximum Number of Messages to be sent in response to the current QUERY_LOG message. If non-zero then this limits the total number of message that can be sent from the log. If zero then the number of messages sent from the log has no limit. Applicable if Time range is not ‘Z’. |
| K | Last Message: ‘1’ = automatically include the last message in the log regardless of the filter settings, ‘0’ = don’t automatically include the last message in the log. |
| LLLL | GPS week number of starting date |
| MMMMMM | GPS seconds into week of starting date. |
| NNNN | GPS week number of ending date. 'Most recent' if not present. |
| OOOOOO | GPS seconds into week of ending date. 'Most recent' if not present. |

Table 30, QUERY_LOG Message

### QUERY_POSITION

This message is used to command the TrimTrac device to report either its current or its most recently logged position.

The unit will compute and report new position fix if the QUERY_POSITION Operation Mode is set ‘S’=Compute. The unit will respond by sending a new REPORT_POS message (with TriggerType set to ‘3’=Query); provided, however, that the TrimTrac locator was able to compute a new position fix prior to the GPS Fix Timeout expiring.

The unit will send a single SMS message containing a new STATUS_MSG and the most recently logged REPORT_POS if:

- 1.	The QUERY_POSITION has the Operation Mode set ‘L’=Logged; OR

2.	The QUERY_POSITION has the Operation Mode set ‘S’=Compute, but there has been no motion since the last logged position (i.e. Position Aged is set 0); OR

3.	The QUERY_POSITION has the Operation Mode set ‘S’=Compute and there has been motion since the last logged position (i.e. Position Aged is set 1), but the unit was unable to compute a new position fix.

The new STATUS_MSG will have the TriggerType set to “3”=Query and Position Aged state set ‘1’=Aged indicating there had been motion since the last logged position.

| >QTKABCCCC;PW=PPPPPPPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | Always ‘D’ |
| B | Position Query Mode. S=Compute and report current position; L=Status Report with Last logged position |
| CCCC | Position Query Fix Timeout. In Seconds (10-3600). Note: Temporarily overrides current FIX Timeout, T2, if Position Query Mode set to “S=Compute” and report current position. Settings longer than 600 minutes are generally not recommended. No default value. |
| PPPPPPPP | Security Password. Always 8 alphanumeric characters, UPPER CASE ONLY. . Default 00000000 |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 31, QUERY_POSITION Message

## Position, Status and Response Messages

### REPORT_POS and STATUS_MSG

These two messages are the most common.  The difference between the REPORT_POS and STATUS_MSG is that the REPORT_POS message contains position information. STATUS_MSG does not contain any position.

| >RTKABBBBCDDDEFFFFGGGGGGSTVOPQRUUUUU[HHHIIIIIIIJJJJKKKKKKKLLLLLLMMMNNN];ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Report Type: ‘P’ = Position Report ‘S’ = Status Report |
| BBBB | Protocol Sequence Number. 16-bit Hex (0000-FFFF) incrementing by 1 for each logged report. |
| C | TriggerType 0=IDLE Timeout, T1 1=Motion Detected 2=Alert (VAM-Only) 3=Query 4=Scheduled Report |
| DDD | Battery Level. 0-100%. |
| E | Battery Changed Flag. T=True F=False |
| FFFF | GPS Week Number. Always 4 Digits |
| GGGGGG | GPS Seconds into Week. Always 6 Digits. |
| S | GPS Status Code. 0=3D GPS Fix 1=2D GPS Fix 2=Fix Timeout, 0 SVs 3=Fix Timeout, 1 SV 4=Fix Timeout, 2 SVs 5=Fix Timeout, 3 SVs 6=GPS Error 7=No Fix attempted (Status Message only due IDLE Timeout, T1, expiration) |
| T | GSM Status Code 0=Network Available 1=Message Logged(i.e. Report Delay Flag set=1) 2=Network Timeout 3=SIM Error / No SIM 4=SIM PIN Error 5=Pre-TX log (Low battery) |
| V | Position Age: 0=Current (i.e. no motion since last position) 1=Aged (i.e. motion has occurred since last position) |
| O | HPA State: 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| P | MPA State: 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| Q | LPA State: 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| R | External Power: 0=Below 5 VDC (Bad); 1=(Good) |
| UUUUU | Reserved for future use |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |
|  | Optional (Provided only if Position Report) |
| HHH.IIIIIII | Latitude. WGS-84 Coordinates. Units of Degrees to 7 decimal places plus ‘+’ sign = North and ‘-‘ = South. (-90.0000000 to +90.0000000) |
| JJJJ.KKKKKKK | Longitude. WGS-84 Coordinates. Units of Degrees to 7 decimal places plus ‘+’ sign = East and ‘-‘ = West. (-180.0000000 to +180.0000000) |
| LLLLLL | Altitude. WGS-84 Altitude reference to MSL. In Feet, always 5 Digits plus sign (-99999 to +99999) |
| MMM | Horizontal Speed. Miles Per Hour. Always 3 Digits. |
| NNN | Heading. Relative to True North, increasing Easterly. Units of Degrees. Always 3 Digits. (000-359). |

Table 32, REPORT_POS and STATUS_MSG Messages

Each new outbound REPORT_POS and STATUS_MSG message is given a Report Sequence number.  The sequence number is 16 bits and increments by one with each message created and rolls over to 0000 once the maximum 16 bit value of FFFF is reached.  The TrimTrac Application saves the message in non-volatile memory each time one is created; this is called the Message Log.  The Message Log is a FIFO log of the last 128 REPORT_POS or STATUS_MSG messages (whether transmitted or only logged) such that when it is full the oldest one is deleted.  The Message Log can be queried with the QUERY_LOG message from the server application.

### RESP_ALERT_STATE

This message is sent by the TrimTrac locator after a SET_ALERT_STATE request is received and processed.

| >RTKABCD;ID=YYYYYYYY;*ZZ< |
| --- |
| A | Always ‘L’: Indicates operation mode setting |
| B | HPA State. 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| C | MPA State. 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| D | LPA State. 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 33, RESP_ALERT_STATE Message

### RESP_APP_CONFIG

This is the response message to the SET_APP_CONFIG and QUERY_CONFIG messages containing the Application Parameter values.

| >RTKABBBBBBCCCCCCDDDDDDEEEEEEFFFFFFGGGTTHIJKLLLLMMMMMMNPP;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘A’ = Application Parameters |
| BBBBBB | IDLE Timeout, T1. In seconds (10 – 999990) |
| CCCCCC | FIX Timeout, T2. In seconds (10 – 3600) |
| DDDDDD | TRANSMIT Timeout, T3. In seconds (10 – 3600) |
| EEEEEE | DELAY Timeout, T4. In seconds (10 – 86400) |
| FFFFFF | QUERY Timeout, T5. In seconds (10 – 3600) |
| GGG | Almanac Timeout, T6. In hours (10 – 990) |
| TT | IDLE Wakeup Motion Timeout, T7. In seconds (0 – 90). Note: T7 is used exclusively while in the IDLE state; however, it is superseded by Rolling Motion Window, T21, whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Timeout, T7, must always be set greater than or equal to IDLE Wakeup Motion Second Count; else unit may not exit IDLE state due to motion. |
| H | Motion Report Flag. 0=None; 1=Report first motion before GPS fix |
| I | Report Delay Flag. 0=Transmit All Messages; 1=Transmit NO Messages; 2=Transmit Motion-related Messages-only; 3= Transmit IDLE Timeout, T1 Status Messages-only |
| J | Diagnostics Mode. 0= None; 1= LED |
| K | Communication Mode. 0= SMS; 1= Future |
| LLLL | Battery Change Week. |
| MMMMMM | Battery Change Seconds into Week. |
| N.PP | Firmware version number. |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 34, RESP_APP_CONFIG Message

### RESP_EXT_APP_CONFIG

This is the response message to the SET_EXT_APP_CONFIG and QUERY_CONFIG message containing the Extended Application Parameter values.

| >RTKABCCCCCCDEFFFFFFGGGGGGHIJJJKKKLLMMNNO;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘X’ = Extended Application Parameters |
| B | Scheduled Reporting Mode. 0=None; 1=Daily; 2=Weekly |
| CCCCCC | Scheduled Report Time, T18. In Seconds (0-604799). Note: This is either the seconds into the day or into the week for the device to schedule a report when this feature is enabled. If Scheduled Reporting Mode is set “0=None”, then enter 0. |
| D | DELAY State Query Mode. 0=Disabled; 1=Enabled. Note: If set to “1=Enabled”, the unit does not power off during Delay state. |
| E | IDLE State Query Mode. 0=Disabled; 1=Stationary; 2=Vigilant. Default 0. Note: DELAY State Query Mode is treated as always 1=Enabled when IDLE State Query Mode is set to 2=Vigilant. |
| FFFFFF | IDLE Stationary Mode Wakeup, T19. In Seconds (10-999990). Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to “1=Stationary”. Default 3600. Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to 1=Stationary. |
| GGGGGG | IDLE Stationary Mode Query Timeout, T20. In Seconds (0, 10-3600). Note: Determines how long the unit dwells in the QUERY state each time IDLE Stationary Mode Wakeup, T19, expires. A value of zero causes the QUERY Timeout, T5, value to be used. Default 60. |
| H | Query Hold Flag. 0=Disabled; 1=Enabled. Note: Unit attempts to reconnect to the GSM network if the connection is lost during the QUERY state prior to the expiration of QUERY Timeout, T5. |
| I | DELAY State Extended Motion Detection. 0=Disabled; 1=Enabled. Note: Allows the unit to filter spurious motion detections in DELAY state when set to “1=Enabled”. The unit does not power off during DELAY state and power consumption will increase. |
| JJJ | Position Report Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts. |
| KKK | Status Message Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts. |
| LL | IDLE Wakeup Motion Second Count. In Seconds (1-90). Note: This parameter is used only while IDLE Wakeup Motion Timeout, T7, is running. It is superseded by Rolling Motion Second Count whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Second Count must always be set equal to or less than IDLE Wakeup Motion Timeout, T7; else unit may not exit IDLE state due to motion. Default 1. |
| MM | Rolling Motion Window, T21. In Seconds (1-90). Note: T21 applies in all states except IDLE and FIX; provided, however, that is also automatically enabled for IDLE state whenever IDLE State Query Mode is set “2=Vigilant” OR when IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: Rolling Motion Window, T21, must always be set equal to or greater than Rolling Motion Second Count; else the unit may not exit QUERY state. Default 20. |
| NN | Rolling Motion Second Count. In Seconds (1-90). Note: This parameter is enabled only when Rolling Motion Window, T21, is active. Default 10. |
| O | Motion Override. 0=Normal; 1=Motion Always; 2=Motion Never. Note: Overrides the motion sensor if set to a value other than “0=Normal”. If set to “1=Motion” Always, then the state machine will override the motion sensor such that the unit operates as if motion is always present. If set to “2=Motion Never”, then the state machine will ignore all motion and never generate a fix until the configuration is changed or otherwise commanded to do so (see QUERY_POSITION message). Default 0. |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 35, RESP_EXT_APP_CONFIG Message

### RESP_GPS_CONFIG

This is the response message to the SET_GPS_CONFIG and QUERY_CONFIG message containing the GPS Configuration.

| >RTKABBCCCDDDEEEF;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘G’ = GPS Parameters |
| BB | GPS Elevation Mask. In degrees (0-30) |
| CCC | GPS PDOP Mask. In tenths of PDOP (60 – 200) |
| DDD | GPS PDOP Switch. In tenths of PDOP (40 – 120) |
| EEE | GPS Signal Level. In tenths of AMUs (10 – 80) |
| F | GPS Dynamics Mode. 5=Automobile |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 36, RESP_GPS_CONFIG Message

### RESP_PROV_CONFIG

This is the response message to the SET_PROV_CONFIG and QUERY_CONFIG message containing the provisioning information.

| >RTKABBBBBBBBBBBBBBBBBBBBBBBB;ID=YYYYYYYY;*ZZ< |
| --- |
| A | TrimTrac Configuration Set: ‘V’ = Application Provisioning Parameters |
| BBBBBBBBBBBBBBBBBBBBBBBB | Destination Address. 24 characters including international dialing “+” sign and country code. Field padding in spaces before the international dialing “+” sign |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 37, RESP_PROV_CONFIG Message

### RESP_QUERY_AGGR

This message is sent by the TrimTrac locater after a QUERY_LOG request is received and processed, and if Aggregate Log Reporting Flag is ‘enabled’. It will contain messages in aggregated format as shown below. The entire message can be no more than 160-byte SMS message.

| >RTKA{B};ID=YYYYYYYY;*ZZ< |
| --- |
| A | ‘1’ to ‘4’: Indicates number of REPORT_POS messages contained in this RESP_QUERY_AGGR message. |
| B | Message fields from Report Type to the first semi-colon (excluded). |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 38, RESP_Query_AGGR Message

### RESP_QUERY_LOG

This message is sent after a QUERY_LOG request is received and processed.  It will contain the number of messages actually retrieved from the Message Log and sent to the server application.

| >RTKABBBB;ID=YYYYYYYY;*ZZ< |
| --- |
| A | Always ‘R’: Indicates a response to a QUERY_LOG |
| BBBB | Number of message sent from the log. |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 39, RESP_QUERY_LOG Message

### RESP_VAM_APP

This is the by the TrimTrac locator in response to the SET_VAM_APP_CONFIG and QUERY_CONFIG message.

| >RTKABBBBBBCCCCCCDDDDDDEEEEEEFFFFFFGGGGGGHHHHHHIIIJJJKKKLMN;ID=YYYYYYYY;*ZZ< |
| --- |
| A | VAM-only Configuration Set: ‘Y’ = VAM-only Parameters |
| BBBBBB | HPA Idle Timeout, T11. In Seconds (10-999990) |
| CCCCCC | MPA Idle Timeout, T12. In Seconds (10-999990) |
| DDDDDD | HPA Delay Timeout, T13. In Seconds (10-86400) |
| EEEEEE | MPA Delay Timeout, T14. In Seconds (10-86400) |
| FFFFFF | HPA Transmit Timeout, T15. 0=Infinity; Else in Seconds (10-999990) |
| GGGGGG | MPA Transmit Timeout, T16. 0=Infinity; Else in Seconds (10-999990) |
| HHHHHH | HPA Query Timeout, T17. In Seconds (10-3600) |
| III | HPA Transmit Attempts. 0=Until T15 Expires; 1-255=Number of Tx Attempts |
| JJJ | MPA Transmit Attempts. 0=Until T16 Expires; 1-255=Number of Tx Attempts |
| KKK | LPA Transmit Attempts. 0=Until T3 Expires; 1-255=Number of Tx Attempts |
| L | Ignore HPA. 0=Do NOT Ignore; 1=Ignore |
| M | Ignore MPA. 0=Do NOT Ignore; 1=Ignore |
| N | Ignore LPA. 0=Do NOT Ignore; 1=Ignore |
| YYYYYYYY | Unit ID. Always 8 alphanumeric characters, UPPER CASE ONLY |
| ZZ | Checksum. |

Table 40, RESP_VAM_APP Message

# Technical Tips and Troubleshooting

## Introduction

The TrimTrac locator is designed to operate in the conditions outlined in the Specifications chapter on page 68.

When used and maintained properly, the TrimTrac locator provides years of trouble-free service. The TrimTrac locator has no user-serviceable parts other than its replaceable batteries.

Should the TrimTrac locator fail to operate properly, the user or service technician should troubleshoot the installation before returning any components for repair. If a component fails, return the TrimTrac locator to the authorized Service and Repair Center for repair.

This chapter provides some guidelines for troubleshooting common problems associated with the TrimTrac locator’s operation.  Potential operating problems might include:

Dead Batteries

Poor contact between the Battery Pack and TrimTrac

Poor GPS reception

Poor GSM coverage

Communication failure with base

TrimTrac locator Application programming errors

If the TrimTrac locator continues to operate poorly after you follow the troubleshooting guidelines described in this chapter, contact your TrimTrac locator supplier for assistance.

### Battery Problems

Make sure your batteries are generating sufficient current to power your TrimTrac locator.  Make sure the Battery Pack hold down screw is tight and that the mating spring loaded contacts on the TrimTrac device are not damaged.

### GPS Reception Problems

Even though the TrimTrac locator uses enhanced GPS sensitivity technology, it is still advisable to position the device with as clear of a view of the sky as possible.  Make sure that the TrimTrac locator is reasonably positioned to receive GPS signals.

### GPS Almanac Collection

When the TrimTrac locator is used for the first time after being provisioned, the unit may not have a complete or current GPS almanac.  The unit is allowed up to 15 minutes to collect an almanac after it has computed its first fix.  In other words, the TrimTrac locator can dwell in the FIX state for up to 15 minutes plus T2 seconds before transitioning to the STATUS state.  This will occur whenever the almanac is either incomplete or out of date (i.e. more than T6 seconds old).  During this almanac collection process, users may notice that it takes longer than usual for the unit to transition through the FIX state.  Under normal conditions, it may take on average 45-60 seconds to get a GPS position fix and complete the FIX state; however, this compares to as long as 20 minutes (15 minutes plus 5 minute default T2).  To facilitate the process of almanac collection, it is recommended that the TrimTrac be placed in an area with a clear view of the sky and not be moved until it has completed its first FIX state.

### Location

The TrimTrac locator should be installed as close as possible to horizontal plane, preferably with a reasonably clear view of the horizon and sky. If something on the vehicle—for example, the air conditioning unit on a cab or the trailer connected to a tractor—blocks a significant portion of the horizon and the GPS signals, the GPS receiver will take longer to acquire enough satellites for a position fix. If the TrimTrac locator frequently times out before completing a position fix, try moving the TrimTrac locator to a new location where it is not blocked as much.

### GPS Jamming

The TrimTrac locator should be installed as far away as possible from transmitting antennas, including satellite communication, radar, VHF and cellular. These transmitters may emit jamming signals that interfere with the GPS receiver’s ability to track GPS satellite signals. Generally, the stronger the other transmitting device, the wider the distance required between antennas. For the TrimTrac locator, Trimble recommends a minimum clearance of 46 cm (approximately 18 in.) from these transmitting devices.

Land-based transmitters, including microwave and television transmitters, can also interfere with GPS reception. If the TrimTrac locator is operating near an antenna farm, the TrimTrac locator may temporarily lose GPS reception while in the vicinity of the transmitters. Reception should return once the TrimTrac locator moves away from the transmitters. If your GPS signals are being jammed and moving does not correct the situation, the source of the jamming signal may be another antenna mounted too close to your TrimTrac locator. If possible, turn off the equipment using other nearby antennas to see if this corrects the problem. If turning off nearby equipment un-jams your GPS signals, you need to relocate one or more of the jamming antennas.

### Poor GSM Coverage

Check to make sure the SIM is not missing or incorrectly installed, or the PIN number configured in the TrimTrac does not match the PIN in the SIM. Do the following:

- Insert a SIM if none is present.

- Remove and reinsert the existing SIM to verify proper installation.

- Check the TrimTrac locator configuration to ensure the correct PIN is programmed.

### TrimTrac Locator Location

The TrimTrac locator should be used as close as possible to horizontal plane, preferably with reasonably unobstructed clearance around the unit. If the current location is suspect:

Try another location; and/or

Try a known-good TrimTrac locator or mobile phone

Even in areas with strong GSM service, there may be pockets where GSM service is poor or nonexistent due to how the carrier builds the network. Contact your local service provider for information on GSM coverage.

### GSM Jamming

The TrimTrac locator should be installed as far away as possible from other transmitting antennas including satellite communication, radar, and VHF radio. These transmitters may emit jamming signals that interfere with the GSM phone’s ability to track the GSM signal. If there are other transmitting antennas located on the vehicle, try moving the TrimTrac locator farther away from these antennas. Generally, the stronger the other transmitting device, the wider the distance required between antennas.

### No Data Communication with Base

Check the conditions described in following sections if the TrimTrac locator cannot communicate with the base and:

- You can see that it enters the Transmit and Query modes.

- You have verified that it is calling the correct number.

### Base Modem Configuration

Consult your modem manual for configuration instructions. Each modem manufacturer has its own settings and control commands. Verify that your configuration, PIN numbers, and so on, are correct.

### Defective TrimTrac Locator

To confirm that a TrimTrac locator is defective, do the following:

1.	Try a known good TrimTrac locator.

2.	 Move into an area with strong GSM coverage.

3.	Send the TrimTrac locator an SMS message requesting a response.

Note – Before returning the TrimTrac locator, be sure to save the TrimTrac locator’s configuration settings, and remove your SIM

### No Modem Connection with Server Application

If it appears that you have no modem connection with the Server Application, confirm that the Server Application modem is configured correctly and that the TrimTrac locator is configured and operating correctly. Do the following:

1.	Check to see if the Destination Address is programmed correctly.

2.	Verify the Server Application software is calling the correct TrimTrac locator telephone number and using the correct Unit ID, Security Password and, if required by the SIM card, the SIM PIN.

### TrimTrac Not Reporting

If it appears that the TrimTrac locator is not reporting to the server application as expected, diagnose as follows:

- Configuration.  Always check to confirm whether the TrimTrac locator is configured as appropriate for the particular application environment.  Correct and re-test as necessary.

- Lost Reports.  In this case, the TrimTrac locator has successfully created a new message (Position, Status, or Alert) and it has been sent to the GSM network.  If such sent messages are not received by the server application, then perhaps there is insufficient GSM coverage and/or the messages are getting lost in the GSM network.

Review the TrimTrac locator message log and Report Sequence Numbers compared to those received by the server application.  If there are missing on inconsistent Report Sequence Numbers at the server application vis-à-vis the messages logged within the TrimTrac, then a problem associated with the GSM network is the likely culprit;

- Unsent Reports.  This is when the TrimTrac locator is correctly generating position and status messages, but they are not being sent by the TrimTrac locator, due either to insufficient GSM coverage or the Report Delay Flag is not set to one (1).  Note the Report Delay Flag has no effect on the sending of Alert messages;

- No Reports Generated.  The TrimTrac locator is expected to spend a majority of its time in either the IDLE or DELAY states, during which the unit will not send any messages until motion causes a transition, the appropriate RTC-based timeouts have expired or if an Alert condition occurs.  Another possible cause would be the motion detector and associated latches may not be recognizing Valid Motion; in which case, the unit may dwell in IDLE indefinitely.

### Server Application Software

Confirm the proper Server Application software setup.  The Server Application software may not be correctly integrated with the TrimTrac locator. Contact your software vendor for assistance.

### Verify Checksums when Analyzing Data

An easy way to analyze data received from The TrimTrac locator is to log the actual messages into a text file and verify that the messages are valid by checking the checksums.  Available from www.trimtrac.com is a simple checksum checker executable that can be run against a text file containing messages sent from a TrimTrac locator.  If the checksum contained in the message is “Bad” then the program will indicate it as “BAD” and return what the correct checksum should have been.  Verifying checksums helps avoid wasted time spent evaluating invalid messages.

### Updating Firmware in the Field

You can upload new firmware from a PC or laptop connected to the Provisioning Module. For more information on updating firmware in the field, please consult with your Trimble technical support representative.

### LED Indicator

The LED indicator is useful for diagnosing problems. For more information, see LED States, page 12. If you detect a problem, then have the TrimTrac locator inspected by qualified service personnel.

### Responding to Query SMS messages

The TrimTrac locator processes and responds immediately to any SMS message that it receives while in the QUERY state.  It does not need to cycle back through the State Machine before a response is sent back to the server application.

The TrimTrac locator, however, will not respond to SMS messages that are invalid (i.e. incorrect format, checksum, Unit ID, Security Password and, if used, SIM PIN).

Different network operators may also handled queued up SMS messages differently.  For instance, if the TrimTrac happens not to be in the QUERY state when the server application sends a SMS message, this SMS message will be held at the network operator’s Short Message Service Center (SMSC) for future delivery.  In some cases, the longer the SMS is held at the SMSC, the lower in the delivery priority the message may become.  As a consequence, the SMSC may not send the queued SMS message before the QUERY Timeout, T5, T5, has expired.  Therefore, if it can be reasonably expected that an application will have extended periods of time between QUERY states, then extending the QUERY Timeout, T5, should be considered.

# Specifications

### GSM Specifications

GSM 900/1800/1900 MHz

Normal MS – SMS Data Only

Class 4 (2W) @ 900 MHz (EGSM)

Class 1 (1W) @ 1800 MHz (GSM 1800) and 1900 MHz (GSM 1900 PCS)

Subscriber Identity Module

1.8/3.0 Volt

Type Approvals

FCC Part 15, FCC Part 24

Industry Canada

CE MARK

EC R&TTE Type Examination

### GPS Specifications

General

L1 (1575.42 MHz) frequency, C/A code

12-Channels, 48 Correlators

Sensitivity

Minimum –136.0 dBm Acquisition without any external assistance.

Accuracy

Horizontal:  <  6 meters (50%)

Altitude:      <11 meters (50%)

Acquisition

Signal Power     -130.0 dB	-136.0 dB

Hot Start (50%)	<24 sec

Warm Start (50%)<38 sec	<400 sec

Cold Start (50%)	<90 sec

Dynamics

Acceleration: 4g (39.2 m/sec2)

Motional jerk: 20 m/sec3

### Environmental Specifications

Temperature

Operating: -10oC to + 55oC

Humidity

5% to 95% RH non-condensing @ +40oC

Vibration*

0.008 g2/Hz    5 Hz  to   20  Hz

0.05g2/Hz       20 Hz to 100 Hz

-3 dB/octave 100 Hz to 900 Hz

Shock*

Operational:   40g for 11mSec

Non-operational:

75g for  6 mSec

* = Requires Vehicle Adapter Module

### Physical Specifications

Assembly

Injection molded plastic with integrated battery pack

Size

133 mm x 64 mm x25 mm

5.25” x 2.5” x1.0”

Weight

102 grams ( 3.6 oz) not including batteries

# Bibliography

European Telecommunications Standards Institute (ETSI). ETSI is the standards body for GSM worldwide operations. Specifications on various aspects of GSM phone operations (AT commands, installation requirements, and terminology) are available for download from ETSI at: www.etsi.org

GPS, A Guide to the Next Utility, Trimble P/N 18239 (1992). A short, non-technical introduction to GPS. Explains what GPS does, how it works, and its capabilities and limitations. www.trimble.com

GSM Made Simple, by George Lamb published by Cordero Consulting and Regal Printing, Atlanta GA, 1997 (ISBN 0-966-57520-2).

GSM World. The GSM World site has information on the technical and business aspects of GSM. Contact information is available for GSM carriers as well as GSM hardware manufacturers. www.gsmworld.com

ICD-GPS-200. NAVSTAR GPS Space Segment: Navigation User Interfaces, drawing number ICD-GPS-200 (3 July 1991). The official definition of the data formats used in NAVSTAR GPS satellite signals. www.navcen.uscg.gov/gps

Commanding Officer

USCG NAVCEN

7323 Telegraph Road

Alexandria, VA 22315

703-313-5900

Proceedings of the Institute of Navigation, Washington DC. A series of three volumes of papers describing GPS Theory published between 1980 and 1986 by the Institute of Navigation. Essential source material for system designers. www.ion.org

SAE J1455 Joint SAE/TMC Recommended Environmental Practices for Electronic Equipment Design (Heavy Duty Trucks). www.sae.org

# Glossary

The Glossary defines technical terms and abbreviations used in this manual. It includes terms from the fields of wireless communications and GPS technology.

0D

Time only in GPS terminology.

2D

Two dimensions and time in GPS terminology.

3D

Three dimensions and time in GPS terminology.

2D

GPS Two-dimensional GPS position fix and time.

3D

GPS Three-dimensional GPS position fix and time.

Altitude

Height above mean sea level (MSL).

ASCII

American Standard Code for Information Interchange.

C/A

Coarse Acquisition code used to receive GPS signals with receivers designed operate using SPS (Standard Positioning Service).

Checksum

The message checksum field provides for a two-digit hexadecimal checksum value, which is computed by XOR’ing all characters from the beginning of the sentence up to and including the * character. The checksum is always the last element of the sentence before the message < delimiter. The use of checksums can help in instances where the communication channel is noisy.

ETSI

European Telecommunications Standards Institute.

GPS

Global Positioning System.

GSM

Global System for Mobile communications.

HPA

High Priority Alert

IMEI

International Mobile Equipment Identity.

IMSI

International Mobile Subscriber Identity.

Latitude

Latitude coordinate of position fix with positive value indicating North.

LED

Light-Emitting Diode.

Longitude

Longitude coordinate of position fix with positive value indicating East.

LPA

Low Priority Alert

MPA

Medium Priority Alert

PC

Windows (2000, XP)-compatible Personal Computer.

PCS

Personal Communications Service.

PIN

Personal Identity Number.

RF

Radio Frequency.

SIM

Subscriber Identity Module.

SMPP

Short Message Peer to Peer.

SMS

Short Message Service.

SPS

Standard Positioning Service.

TAIP

Trimble ASCII Interface Protocol.

## Basic Feature Parameter Ranges and Default Settings

| Parameter | Unit/Notes | Default |
| --- | --- | --- |
| Unit ID | Unique unit identifier. Always 8 alphanumeric characters, UPPER CASE ONLY, and can only be changed using Provisioning Module. | 00000000 |
| Destination Address | Valid destination address for SMS messages must be entered prior to initial deployment. 24 characters including international dialing “+” sign and country code. | <Empty> |
| SIM PIN | Entered only if required by SIM card and can be entered or changed using Provisioning Module. If used, must be between 4 and 8 digits. | <Empty> |
| Security Password | Always 8 alphanumeric characters, UPPER CASE ONLY. Non-default entries can only be made using Provisioning Module. | 00000000 |
| IDLE Timeout, T1 | In seconds (10 – 999990) | 43200 |
| FIX Timeout, T2 | In seconds (10 – 3600) | 300 |
| TRANSMIT Timeout, T3 | In seconds (10 – 3600) | 120 |
| DELAY Timeout, T4 | In seconds (10 – 86400) | 900 |
| QUERY Timeout, T5 | In seconds (10 – 3600) | 60 |
| Almanac Timeout, T6 | In hours (10 – 990) | 168 |
| IDLE Wakeup Motion Timeout, T7 | In seconds (0 – 90). Note: T7 is used exclusively while in the IDLE state; however, it is superseded by Rolling Motion Window, T21, whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Timeout, T7, must always be set greater than or equal to IDLE Wakeup Motion Second Count; else unit may not exit IDLE state due to motion. | 15 |
| Motion Report Flag | 0=None; 1=Report first motion before GPS fix | 0 |
| Report Delay Flag | 0=Transmit All Messages; 1=Transmit NO Messages; 2=Transmit Motion-related Messages-only; 3= Transmit IDLE Timeout, T1 Status Messages-only | 0 |
| Diagnostics Mode | 0= None; 1= LED | 1 |
| Communication Mode | 0= SMS; 1= Future | 0 |
| GPS Elevation Mask | In degrees (0-30) | 5 |
| GPS Signal Level Mask | In tenths of AMUs (10 – 80) | 10 |
| GPS PDOP Mask | In tenths of PDOP (60 – 200) | 120 |
| GPS PDOP Switch | In tenths of PDOP (40 – 120) | 60 |
| GPS Dynamics Mode | 5=Automobile | 5 |

Table 41, Basic Feature Parameters and Defaults

## Enhanced Feature Parameter Ranges and Default Settings

| Parameter | Unit/Notes | Default |
| --- | --- | --- |
| Scheduled Reporting Mode | 0=None; 1=Daily; 2=Weekly | 0 |
| Scheduled Report Time, T18 | In Seconds (0-604799). Note: This is either the seconds into the day or into the week for the device to schedule a report when this feature is enabled. If Scheduled Reporting Mode is set “0=None”, then enter 0. | 0 |
| DELAY State Query Mode | 0=Disabled; 1=Enabled. Note: If set to “1=Enabled”, the unit does not power off during Delay state. | 0 |
| IDLE State Query Mode | 0=Disabled; 1=Stationary; 2=Vigilant | 0 |
| IDLE Stationary Mode Wakeup, T19 | In Seconds (10-999990). Note: Determines the frequency at which the QUERY state is enabled while in the IDLE state if and only if the IDLE State Query Mode is set to “1=Stationary”. | 3600 |
| IDLE Stationary Mode Query Timeout, T20 | In Seconds (0, 10-3600). Note: Determines how long the unit dwells in the QUERY state each time IDLE Stationary Mode Wakeup, T19, expires. A value of zero causes the QUERY Timeout, T5, value to be used. | 60 |
| Query Hold Flag | 0=Disabled; 1=Enabled. Note: Unit attempts to reconnect to the GSM network if the connection is lost during the QUERY state prior to the expiration of QUERY Timeout, T5. | 0 |
| DELAY State Extended Motion Detection | 0=Disabled; 1=Enabled. Note: Allows the unit to filter spurious motion detections in DELAY state when set to “1=Enabled”. The unit does not power off during DELAY state and power consumption will increase. | 1 |
| Position Report Transmit Attempts | 0=Until T3 Expires; 1-255=Number of Tx Attempts | 1 |
| Status Message Transmit Attempts | 0=Until T3 Expires; 1-255=Number of Tx Attempts | 1 |
| IDLE Wakeup Motion Second Count | In Seconds (1-90). Note: This parameter is used only while IDLE Wakeup Motion Timeout, T7, is running. It is superseded by Rolling Motion Second Count whenever IDLE State Query Mode is set “2=Vigilant” OR while IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: IDLE Wakeup Motion Second Count must always be set equal to or less than IDLE Wakeup Motion Timeout, T7; else unit may not exit IDLE state due to motion. | 1 |
| Rolling Motion Window, T21 | In Seconds (1-90). Note: T21 applies in all states except IDLE and FIX; provided, however, that is also automatically enabled for IDLE state whenever IDLE State Query Mode is set “2=Vigilant” OR when IDLE Stationary Mode Query Timeout, T20, is running due to IDLE State Query Mode being set “1=Stationary”. WARNING: Rolling Motion Window, T21, must always be set equal to or greater than Rolling Motion Second Count; else the unit may not exit QUERY state. | 20 |
| Rolling Motion Second Count | In Seconds (1-90). Note: This parameter is enabled only when Rolling Motion Window, T21, is active. WARNING: Rolling Motion Second Count must always be set equal to or less than the setting for Rolling Motion Window, T21; else the unit may not exit QUERY state. | 10 |
| Motion Override | 0=Normal; 1=Motion Always; 2=Motion Never. Note: Overrides the motion sensor if set to a value other than “0=Normal”. If set to “1=Motion” Always, then the state machine will override the motion sensor such that the unit operates as if motion is always present. If set to “2=Motion Never”, then the state machine will ignore all motion and never generate a fix until the configuration is changed or otherwise commanded to do so (see QUERY_POSITION message). | 0 |
| Position Query Mode | S=Compute and report current position; L=Status Report with Last logged position. | None |
| Position Query Fix Timeout | In Seconds (10-3600). Note: Temporarily overrides current FIX Timeout, T2, if Position Query Mode set to “S=Compute” and report current position. Settings longer than 600 minutes are generally not recommended. | None |

Table 42, Enhanced Feature Parameters and Defaults.

## Vehicle Adapter Module Parameter Ranges and Default Settings

| Parameter | Unit/Notes | Default |
| --- | --- | --- |
| HPA Idle Timeout, T11 | In Seconds (10-999990) | 10 |
| MPA Idle Timeout, T12 | In Seconds (10-999990) | 10 |
| HPA Delay Timeout, T13 | In Seconds (10-86400) | 10 |
| MPA Delay Timeout, T14 | In Seconds (10-86400) | 10 |
| HPA Transmit Timeout, T15 | 0=Infinity; Else in Seconds (10-999990) | 0 |
| MPA Transmit Timeout, T16 | 0=Infinity; Else in Seconds (10-999990) | 120 |
| HPA Query Timeout, T17 | In Seconds (10-3600) | 60 |
| HPA Transmit Attempts | 0=Until T15 Expires; 1-255=Number of Tx Attempts | 0 |
| MPA Transmit Attempts | 0=Until T16 Expires; 1-255=Number of Tx Attempts | 0 |
| LPA Transmit Attempts | 0=Until T3 Expires; 1-255=Number of Tx Attempts | 0 |
| Ignore HPA | 0=Do NOT Ignore; 1=Ignore | 0 |
| Ignore MPA | 0=Do NOT Ignore; 1=Ignore | 0 |
| Ignore LPA | 0=Do NOT Ignore; 1=Ignore | 0 |

Table 43, Enhanced Feature Parameters and Defaults.

## Read-Only Parameters, Formats and Ranges

| Parameter | Value |
| --- | --- |
| Protocol Sequence Number | 16-bit Hex (0000-FFFF) incrementing by 1 for each logged report |
| TriggerType | 0=IDLE Timeout, T1 1=Motion Detected 2=Alert (VAM-Only) 3=Query 4=Scheduled Report |
| Battery Level | 0-100% |
| Battery Changed Flag | T=True F=False |
| GPS Week Number | Always 4 Digits |
| GPS Seconds into Week | Always 6 Digits |
| GPS Status Code | 0=3D GPS Fix 1=2D GPS Fix 2=Fix Timeout, 0 SVs 3=Fix Timeout, 1 SV 4=Fix Timeout, 2 SVs 5=Fix Timeout, 3 SVs 6=GPS Error 7=No Fix attempted (Status Message only due IDLE Timeout, T1, expiration) |
| GSM Status Code | 0=Network Available 1=Message Logged(i.e. Report Delay Flag set=1) 2=Network Timeout 3=SIM Error / No SIM 4=SIM PIN Error 5=Pre-TX log (Low battery). |
| Position Age | 0=Current (i.e. no motion since last position) 1=Aged (i.e. motion has occurred since last position) |
| HPA State | 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| MPA State | 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| LPA State | 0=Normal; 1=Alert; 2=Sent; 3=Acknowledged |
| External Power | 0=Below 5 VDC (Bad); 1=(Good) |
| Latitude | WGS-84 Coordinates. Units of Degrees to 7 decimal places plus ‘+’ sign = North and ‘-‘ = South. (-90.0000000 to +90.0000000) |
| Longitude | WGS-84 Coordinates. Units of Degrees to 7 decimal places plus ‘+’ sign = East and ‘-‘ = West. (-180.0000000 to +180.0000000) |
| Altitude | WGS-84 Altitude reference to MSL. In Feet, always 5 Digits plus sign (-99999 to +99999) |
| Horizontal Speed | Miles Per Hour. Always 3 Digits |
| Heading | Relative to True North, increasing Easterly. Units of Degrees. Always 3 Digits. (000-359) |

Table 44, Read-only Parameters

Figure 2, VAM Alert Wiring Diagram

# Footnotes

In the United States and Canada, the SAR limit for mobile phones used by the public is 1.6 watts/kg (W/kg) averaged over one gram of tissue.  The standard incorporates a substantial margin of safety to give additional protection for the public and to account for any variations in measurement.