Steps to verify that GPS hardware is enabled:

1.       Steps to verify that GPS hardware is enabled:

a)       While booting the ML900, press F2 to enter the setup utility.

b)       Select Components and check the GPS menu if not already checked.

2.       Steps to verify that GPS is working:

a)     Start SQ_Monitor utility on COM5. The application is located on “d:\ml900 drivers\gps lassen SQ starter kit software tools\sq_monitor v1.02.

b)     Select Initialize ( Factory Reset ( Yes.

c)      Verify that RX and TX status bar indicators are flashing.

d)     Verify that Satellite Data panel is not empty 0 or 0.0 is OK if testing indoors, if data is present go to step 3.

e)      If no data is displayed select Configure ( Serial Port...

f)      The following settings will enable the GPS receiver to communicate with the SQ_Monitor program:

·         Input Protocol: TSIP

·         Output Protocol: TSIP

·         Baud Rate: 9600

·         Data Bits: 8

·         Parity: Odd

·         Stop Bits: 1

g)      Select the Set Button.

h)     Change PC com settings to match ( No.

i)       Do you wish to save the receiver settings to Flash Memory (Yes (OK.

j)       Verify that data is being returned to the SQ_Monitor application (Step d).

3.       Steps to set up the GPS to work with Premier MDC:

a)     Select Configure ( Serial Port...

b)     The following settings will enable the GPS receiver to communicate with PMDC. The only setting that is changed from the previous test is “Output Protocol.”

·         Input Protocol: TSIP

·         Output Protocol: TSIP

·         Baud Rate: 9600

·         Data Bits: 8

·         Parity: Odd

·         Stop Bits: 1

c)       Select the Set Button.

d)       Change PC com settings to match ( No.

e)       Do you wish to save the receiver settings to Flash Memory (Yes (OK.